LEVEL CROSSING MAINTENANCE

STANDARD TRAFFIC MANAGEMENT PLAN

To get this standard TMP approved as a generic TMP an STMS needs to:

- Follow the instructions shown in red in the standard TMP

- Submit the completed GTMP to the appropriate road controlling authority for approval

Table of Contents

Level Crossing Maintenance for period (add year of operation)	3

Level Crossing Maintenance Procedures	9

1.	Monthly inspection and maintenance of barriers, bells and alarms	9

2.	Annual inspection and maintenance of barriers, bells and alarms	10

3a	Alignment of signal lenses (lights) LED	11

3b	Alignment of signal lenses (lights) non-LED	12

4	Replacement of lightweight barrier arms	14

5	Barrier not operating	15

6	Signals not operating	16

7	Barriers and signals not operating	17

Appendix 1: KiwiRail site record	18

Appendix 2: STMS List	19

Appendix 3: Traffic Management Diagrams (TMDs)	19

TMD 1 - General maintenance of barriers and signals	20

TMD 2- Annual inspections & maintenance	21

TMD 3a- Alignment of lenses – LED	22

TMD 3b- Alignment of lenses - Non LED	23

TMD 4 - Replacing barrier	24

TMD 5 - Barrier not working	25

TMD 6 - Signals not working	26

TMD 7 -Signals and barrier not working	27

Appendix 4: List of Crossing Locations	28

| Level Crossing Maintenance for period (add year of operation) |
| --- |
| Use this form for complex activities. Refer to the NZ Transport Agency’s Traffic control devices manual, part 8 Code of practice for temporary traffic management (CoPTTM), section E, appendix A for a guide on how to complete each field. |
| Organisations /TMP reference | TMP reference: Insert reference | Contractor: KiwiRail | Principal (Client): New Zealand Railways Corporation |
|  |  |  | RCA: Add name of the RCA that the TMP is to be submitted to |
| Location details and road characteristics | Road names and suburb | House no./RPs (from and to) | Road level | Permanent speed |
|  | All roads where signalised railway level crossings occur (list of crossing locations attached see Appendix 4) | ______________________ | Level LV Level 1 Level 2 | Various |
| Traffic details (main route) | AADT | Peak flows |
|  | Various <10,000 vpd | Peak traffic times are to be avoided as detailed below in the planned work programme |
| Description of work activity |
| Routine maintenance of railway level crossing alarm and barrier systems |
| Planned work programme |
| Start date |  | Time |  | End date |  | Time |  |
| Consider significant stages, for example: road closures detours no activity periods. | Planned work to be undertaken: during daylight hours outside of peak traffic times whenever possible Callouts for faults will be completed at night and at peak times (if needed) |
| Alternative dates if activity delayed | As this is a generic TMP the work activity is to be carried out on an as required basis within agreed times and dates for a 12-month period. Therefore, alternative dates will not be required. |
| Road aspects affected (delete either Yes or No to show which aspects are affected) |
| Pedestrians affected? | No | Property access affected? | No | Traffic lanes affected? | No |
| Cyclists affected? | No | Restricted parking affected? | No | Delays or queuing likely? | No |
| Proposed traffic management methods |
| Installation (includes parking of plant and materials storage) | When approaching the level crossing the driver of the vehicle will: Switch on the vehicles’ amber flashing beacon to indicate the intention to leave the carriageway Indicate Slow down and move into the shoulder/parking area. Once outside the live lane the vehicle will be parked at the furthest lateral position from the edgeline. Amber flashing beacon to remain on and indicator lights in hazard mode, if required, for extra warning. Added protection behind a roadside barrier to be sought and used whenever available to park the vehicle. |
| Attended (day) | A methodology for each activity is provided in the level crossing procedures of this document and in Appendix 3: Traffic management diagrams (TMDS). Where barriers or alarms are used to stop traffic, queues will be monitored continuously. Where queues extend to the WX1R/L (PW57) sign or 5 minutes has passed, work will cease (if on the lane) and the barriers or alarms will be removed and traffic allowed to clear. |
| Attended (night) | A methodology for each activity is provided in the level crossing procedures of this document and in Appendix 3: Traffic management diagrams (TMDS). Where barriers or alarms are used to stop traffic, queues will be monitored continuously. Where queues extend to the WX1R/L (PW57) sign or 5 minutes has passed, work will cease (if on the lane) and the barriers or alarms will be removed and traffic allowed to clear. |
| Unattended (day) | A methodology for each activity is provided in the level crossing procedures of this document and in Appendix 3: Traffic management diagrams (TMDs). |
| Unattended (night) | Methodology for each activity is provided in the level crossing procedures of this document and in Appendix 3: Traffic management diagrams (TMDs). |
| Detour route | Detours will not be required for this work activity. |
|  | Does detour route go into another RCA’s roading network? No (delete either Yes or No) If Yes, has confirmation of acceptance been requested from that RCA? Yes No (delete either Yes or No) Note: Confirmation of acceptance from affected RCA must be submitted prior to occupying the site. |
| Removal | When leaving the site, the driver will: Turn off hazard indicators where used Indicate and wait until there is a gap in traffic Move into the carriageway and accelerate to the permanent speed limit Turn off the indicator and amber flashing beacon. |
| Proposed TSLs (see TSL decision matrix for guidance) |
|  | TSL details as required Approval of Temporary Speed Limits (TSL) are in terms of Section 5 of Land Transport Rule: Setting of Speed Limits 2003, Rule 54001 (List speed, length and location) | Times (From and to) | Dates (Start and finish) | Diagram ref. no.s (Layout drawings or traffic management diagrams) |
| Attended day/night | Temporary speed limits will not be required | _____________ | _____________ | _____________ |
| Unattended day/night | Temporary speed limits will not be required | _____________ | _____________ | _____________ |
| Positive traffic management measures |
| Not required |
| Contingency plans |
| Generic contingencies for: major incidents incidents pre planed detours. Remove any options which do not apply to your job | Major Incident A major incident is described as: Fatality or serious injury - real or potential Significant property damage, or Emergency services (police, fire, etc) require access or control of the site. | Actions The STMS/TC must immediately conduct the following: stop all activity and traffic movement secure the site to prevent (further) injury or damage contact the appropriate emergency authorities render first aid if competent and able to do so notify the RCA representative and / or the engineer under the guidance of the ‘officer in charge’ (police or fire) of the site, reduce effects of TTM on the road or remove the activity if safe to do so re-establish TTM and traffic movements when advised by officer in charge that it is safe to do so. |
|  | Incident An incident is described as: excessive delays - real or potential minor or non-inquiry accident that has the potential to affect traffic flow structural failure of the road. | Actions The STMS/TC must immediately conduct the following: stop all activity and traffic movement if required secure the site to prevent the prospect of injury or further damage notify the RCA representative and / or the engineer STMS to implement a plan to safely remove TTM and to establish normal traffic flow if safe to do so re-establish TTM and traffic movements when it is safe to do so and when traffic volumes have reduced. |
|  | Detour If because of the on-site activity it will not be possible to remove or reduce the effects of TTM once it is established a detour route must be designed. This is likely for: excessive delays when using an alternating flow design for TTM redirecting one direction of flow and / or total road closure and redirection of traffic until such time that traffic volumes reduce and tailbacks have been cleared. The risks in the type of work being undertaken, the risks inherent in the detour, the probable duration of closure and availability and suitability of detour routes need to be considered. The detour and route must be designed including: pre- approval form the RCA’s whose roads will be used or affected by the detour route ensure that TTM equipment for the detour - signs etc are on site an pre-installed. | Actions When it is necessary to implement the pre-planned detour the STMS must immediately undertake the following: Notify the RCA and / or the engineer when the detour is to be established Drive through the detour in both directions to check that it is stable and safe Remove the detour as soon as it practicable and safe to do so and the traffic volumes have reduced and tailbacks have cleared Notify the RCA and / or the engineer when the detour has been disestablished and normal traffic flows have resumed. |
|  | Note also the requirements for no interference at an accident scene: In the event of an accident involving serious harm the STMS/TC must ensure that nothing, including TTM equipment, is removed or disturbed and any wreckage article or thing must not be disturbed or interfered with, except to: Save a life of, prevent harm to or relieve the suffering of any person, or To maintain the access of the general public to an essential service or utility, or To prevent serious damage to or serious loss of property. |
| Other contingencies to be identified by the applicant (i.e. steel plates to quickly cover excavations) | High Traffic volume on-site: Work will not begin until excess traffic has been cleared. Where the work is carried out clear of the carriageway it is unlikely the traffic will be affected. However, at any time when the work activity results in a buildup of traffic, work will cease until traffic has cleared. Access for emergency vehicles: At any time, a crossing is closed to traffic, the crossing will be opened immediately to allow emergency services to pass. Inclement Weather: If visibility is reduced to less than the clear sight distance required for the road user, work will cease until visibility is restored. Traffic accidents on site: These procedures are to be followed in the event of a traffic accident on site: A fire extinguisher and First Aid kit are to be carried in each work vehicle Emergency services to be contacted when required to attend. |
| Authorisations |
| Parking restriction(s) alteration authority | Will controlled street parking be affected? | No | Has approval been granted? | _____ |
|  | __________ |
| Authorisation to work at permanent traffic signal sites | Will portable traffic signals be used or permanent traffic signals be changed? | No | Has approval been granted? | ______ |
|  | __________ |
| Road closure authorisation(s) | Will full carriageway closure continue for more than 5 minutes (or other RCA stipulated time)? | No | Has approval been granted? | _______ |
|  | __________ |
| Bus stop relocation(s) – closure(s) | Will bus stop(s) be obstructed by the activity? | No | Has approval been granted? | _______ |
|  | ___________ |
| Authorisation to use portable traffic signals | Make, model and description/number | ___________ |
|  | NZTA compliant? | Yes (delete either Yes or No) |
| EED |
| Is an EED applicable? | No | EED attached? | No |
| Delay calculations/trial plan to determine potential extent of delays |
| Not required |
| Public notification plan |
| Not required |
| Public notification plan attached? | No |
| On-site monitoring plan |
| Attended day | STMS/TC to record details of the worksite onto the KiwiRail daily site record (Appendix 1) |
| Unattended (day and/or night) | Temporary warning signs will be checked every 24hrs when barriers and or alarms are not working. |
| Method for recording daily site TTM activity (e.g. CoPTTM on-site record) |
| KiwiRail daily site record. |
| Site safety measures |
| All personnel on site will wear high visibility garments. A hazard checklist will be completed and potential traffic hazards identified – site personnel will be briefed on the hazards. All personnel on site will comply with the requirements of the KiwiRail Site Safety Plan. |
| Other information |
| Signals (which include railway bells, lights and barriers) are legal mechanisms for enforcing a compulsory stop of traffic. In extreme cases where traffic must be stopped (e.g. a broken barrier arm) the signals will be used to stop traffic for no more than 5 minutes. The following additional information is provided: Location and layout of local Level Crossings where this TMP will be implemented. |
| Site specific layout diagrams |
| Number | Title |
| 1 | General maintenance of barriers and signal |
| 2 | Annual inspections and maintenance |
| 3a | Alignment of lights. (LED) |
| 3b | Alignment of lights (non LED) |
| 4 | Replacing a barrier arm |
| 5 | Level crossing barriers not operating |
| 6 | Level crossing alarms not operating |
| 7 | Level crossing alarms and barriers not operating |
| Contact details |
|  | Name | 24/7 contact number | CoPTTM ID | Qualification | Expiry date |
| Principal | To be completed for each RCA road network |  |  |  |  |
| TMC | To be completed for each RCA road network |  |  |  |  |
| Engineers’ representative | To be completed for each RCA road network where required |  |  |  |  |
| Contractor | To be completed for each RCA road network |  |  |  |  |
| STMS | Named on KiwiRail daily site record (Appendix 1) |  |  |  |  |
| TC | Named on KiwiRail daily site record (Appendix 1) |  |  |  |  |
| Others as required | _________________________________________ | ____________ | _________ | ____________ | ________ |
| TMP preparation |
| Preparation | To be added | To be added | To be added | To be added | To be added | To be added |
|  | Name (STMS qualified) | Date | Signature | ID no. | Qualification | Expiry date |
| This TMP meets CoPTTM requirements Number of diagrams attached | As per schedule attached |
| TMP returned for correction (if required) |  |  |  |  |  |  |
|  | Name | Date | Signature | ID no. | Qualification | Expiry date |
| Engineer/TMC to complete following section when approval or acceptance required |
| Approved by TMC/engineer (delete one) |  |  |  |  |  |  |
|  | Name | Date | Signature | ID no. | Qualification | Expiry date |
| Acceptance by TMC (only required if TMP approved by engineer) |  |  |  |  |  |  |
|  | Name | Date | Signature | ID no. | Qualification | Expiry date |
| Qualifier for engineer or TMC approval |
| Approval of this TMP authorises the use of any regulatory signs included in the TMP or attached traffic management diagrams. This TMP is approved on the following basis: To the best of the approving engineer’s/TMC’s judgment this TMP conforms to the requirements of CoPTTM. This plan is approved on the basis that the activity, the location and the road environment have been correctly represented by the applicant. Any inaccuracy in the portrayal of this information is the responsibility of the applicant. The STMS for the activity is reminded that it is the STMS’s duty to postpone, cancel or modify operations due to the adverse traffic, weather or other conditions that affect the safety of this site. |
| Notification to TMC prior to occupying worksite/Notification completed |
| Type of notification to TMC required | As agreed with RCA | Notification completed |  |  |  |
|  |  |  | Date |  |  |
|  |  |  | Time |  |  |

# Level Crossing Maintenance Procedures

## Monthly inspection and maintenance of barriers, bells and alarms

| Activity | Duration | Location | Effect on traffic | Proposed TM Method | Relevant Diagram(s) |
| --- | --- | --- | --- | --- | --- |
| Checking and adjusting the operation of all equipment on site. This involves moving between the components of the system and crossing the road to inspect the equipment located on the opposite location. May also include activity (3a) or (3b) Alignment of Signal Lenses (lights) LED/NON LED. | 10mins | At mast location on railway reserve. Minimum 1m clear of the carriageway at all times | NIL | Daylight hours only Inspector will remain clear of the carriageway at all times Work Vehicle must be parked in a position where it will not obstruct the road users’ view of the crossing alarm lights or existing/temporary road signs | 1, 3a, 3b |

## Annual inspection and maintenance of barriers, bells and alarms

| Activity | Duration | Location | Effect on traffic | Proposed TM Method | Relevant Diagram(s) |
| --- | --- | --- | --- | --- | --- |
| Checking and adjusting the operation of all equipment on site. This involves moving between the components of the system and crossing the roads to inspect the equipment located on the opposite location. Barrier arms may need to be lowered to check operation. May also include activity (3a) or (3b) Alignment of Signal Lenses (lights) LED/NON LED | Up to 1 hour | At mast location on railway reserve. Minimum 1m clear of the carriageway at all times | MINOR Short delay when operation of the barrier arm is tested (approximately 1 minute) | Static Operation, Not on a live lane, Daylight hours only Work Vehicle must be parked in a position where it will not obstruct the road users’ view of the crossing alarm lights or existing/temporary road signs | 2, 3a, 3b |

## 3a	Alignment of signal lenses (lights) LED

| Activity | Duration | Location | Effect on traffic | Proposed TM Method | Relevant Diagram(s) |
| --- | --- | --- | --- | --- | --- |
| Checking the alignment of the signal lights. LED lights are non-directional and can be aligned from the supporting mast position. | Up to 10 mins | At mast location on railway reserve. Minimum 1m clear of the carriageway at all times | NIL | Daylight hours only Inspector will remain clear of the carriageway at all times Work Vehicle must be parked in a position where it will not obstruct the road users’ view of the crossing alarm lights or existing/temporary road signs | 3a |

## 3b	Alignment of signal lenses (lights) non-LED

| Activity | Duration | Location | Effect on traffic | Proposed TM Method | Relevant Diagram(s) |
| --- | --- | --- | --- | --- | --- |
| Checking the alignment of the signal lights. Non-LED lights are directional and must be aligned to focus at a particular location on the approaching traffic lane. The inspector (focus checker) is required to check the alignment from a position on the carriageway. This can be achieved by crossing the road at the required point and checking the focus visually as the focus point is reached. | Up to 10 mins Up to 10 seconds crossing the live traffic lane | At mast location on railway reserve. On the carriageway While crossing the road at a point 70m away from the railway crossing | NIL | Daylight hours only Inspector will only enter the carriageway when there is no approaching traffic. Clear sight distance for the activity is to be maintained. Inspector will leave the carriageway on approach of a vehicle. Where clear sight distance cannot be achieved, or in high traffic areas, a spotter will be deployed to warn the focus checker of approaching traffic. The worker adjusting the light may act as the spotter for the person checking the focus under the following conditions; Clear sight distance is available to approaching road users in the direction of the focus checker The spotter is able to communicate easily and immediately with the focus checker. using an RT Work Vehicle must be parked in a position where it will not obstruct the road users’ view of the crossing alarm lights or existing/temporary road signs | 3b |

## 4	Replacement of lightweight barrier arms

| Activity | Duration | Location | Effect on traffic | Proposed TM Method | Relevant Diagram(s) |
| --- | --- | --- | --- | --- | --- |
| The barrier arms are raised to the vertical position, pivoted 90o and lowered parallel with the road. The damaged arm can be replaced in this position without obstructing the carriageway. It may be necessary for the worker to enter the carriageway for up to 2 minutes if the barrier is damaged and it cannot be raised. In this circumstance, the alarms will be operating and traffic will be stopped (Note: to be used if the alarms are also not operating) | Up to 10 mins | At mast location on railway reserve. | MINOR Short delay while operation of the barrier arm is tested approximately 1 minute (less than a typical passing train) | Static Operation, May require access to the carriageway while alarms are in operation Work Vehicle must be parked in a position where it will not obstruct the road users’ view of the crossing alarm lights or existing/temporary road signs | 4 |

## 5	Barrier not operating

| Activity | Duration | Location | Effect on traffic | Proposed TM Method | Relevant Diagram(s) |
| --- | --- | --- | --- | --- | --- |
| Advance warning to be installed at the site to give warning of barrier arms not operating. | Possibly up to several days | On the approach to the non-operational barrier and below the cross bar at the crossing point. | SAFETY COMPROMISED Managed with temporary sign | Temporary warning signs (OTHER HAZARD) and (BARRIERS NOT WORKING) below the existing WX1R/L (PW57) Work Vehicle must be parked in a position where it will not obstruct the road users’ view of the crossing alarm lights or existing/temporary road signs | 5 |

## 6	Signals not operating

| Activity | Duration | Location | Effect on traffic | Proposed TM Method | Relevant Diagram(s) |
| --- | --- | --- | --- | --- | --- |
| Advance warning to be installed at the site to give warning of signals not operating. | Various, possibly up to several days | Across the crossing site. On the approach to the non-operational signals and below the cross bar at the crossing point. | SAFETY COMPROMISED Managed with temporary sign | Temporary warning signs (OTHER HAZARD) and (SIGNALS NOT WORKING) below the existing WX1R/L (PW57) Cover flashing lights at crossing with orange bags Work Vehicle must be parked in a position where it will not obstruct the road users’ view of the crossing signal lights or existing/temporary road signs | 6 |

## 7	Barriers and signals not operating

| Activity | Duration | Location | Effect on traffic | Proposed TM Method | Relevant Diagram(s) |
| --- | --- | --- | --- | --- | --- |
| Advance warning to be installed at the site to give warning of barriers signals not operating. | Possibly up to several days | Across the crossing site. On the approach to the non-operational barriers and signals and below the cross bar at the crossing point. | SAFETY COMPROMISED Managed with temporary sign | Temporary warning signs (OTHER HAZARD), (SIGNALS NOT WORKING) and (BARRIER NOT WORKING) below the existing WX1R/L (PW57) and below the cross bar at the crossing Cover flashing lights at crossing with orange bags Work Vehicle must be parked in a position where it will not obstruct the road users’ view of the crossing alarm lights or existing/temporary road signs | 7 |

# Appendix 1: KiwiRail site record

| KIWIRAIL SITE RECORD To be used to confirm site details. Must be retained for 12 months. | Date |
| --- | --- |
| Person responsible for site | Name | CoTTM ID Number |
|  | Signature | STMS / TC |
| Crossing location | Arrival time | TMD used | Departure time | Initialed |

# Appendix 2: STMS List

Refer to KiwiRail local office for an updated list of STMS for the area

# Appendix 3: Traffic Management Diagrams (TMDs)

| 1 | General maintenance of barriers and signals |
| --- | --- |
| 2 | Annual inspections and maintenance |
| 3a | Alignment of lights. (LED) |
| 3b | Alignment of lights (non LED) |
| 4 | Replacing a lightweight barrier arm |
| 5 | Level crossing barriers not operating |
| 6 | Level crossing alarms not operating |
| 7 | Level crossing alarms and barriers not operating |

## TMD 1 - General maintenance of barriers and signals

## TMD 2- Annual inspections & maintenance

## TMD 3a- Alignment of lenses – LED

## TMD 3b- Alignment of lenses - Non LED

## TMD 4 - Replacing barrier

## TMD 5 - Barrier not working

## TMD 6 - Signals not working

## TMD 7 -Signals and barrier not working

# Appendix 4: List of Crossing Locations

Edit the following list so only those crossing locations relevant to the RCA or region are shown.

| Name | PR Code | Line Name | Metrage | Type |
| --- | --- | --- | --- | --- |
| Ruakura Lane | FLB | ECMT | 4.760000229 | Flashing Lights & Bells |
| Thompsons Track | FLB | MSL | 68.31999969 | Flashing Lights & Bells |
| Stanley Road | FLB | MSL | 84.69999695 | Flashing Lights & Bells |
| Works Road | FLB | MSL | 89.65000153 | Flashing Lights & Bells |
| Compton Street | FLB | MSL | 97.54000092 | Flashing Lights & Bells |
| Lagmhor Road | FLB | MSL | 97.94000244 | Flashing Lights & Bells |
| Winslow Willowby Road | FLB | MSL | 104.1699982 | Flashing Lights & Bells |
| Swamp Road | FLB | MSL | 110.9700012 | Flashing Lights & Bells |
| Delamaine Street | FLB | MSL | 113.0800018 | Flashing Lights & Bells |
| withells Road | FLB | MSL | 126.25 | Flashing Lights & Bells |
| Elizabeth Avenue | HAB | MSL | 67.56999969 | Half arm Barriers with flashing lights and bells |
| South Town Belt | HAB | MSL | 67.98000336 | Half arm Barriers with flashing lights and bells |
| Chertsey Kyle Road | HAB | MSL | 76.31999969 | Half arm Barriers with flashing lights and bells |
| Fairfield Road | HAB | MSL | 88.58000183 | Half arm Barriers with flashing lights and bells |
| East Street | HAB | MSL | 93.27999878 | Half arm Barriers with flashing lights and bells |
| Walnut Avenue | HAB | MSL | 94.23000336 | Half arm Barriers with flashing lights and bells |
| Havelock Street | HAB | MSL | 95.08000183 | Half arm Barriers with flashing lights and bells |
| Moore Street | HAB | MSL | 95.44999695 | Half arm Barriers with flashing lights and bells |
| Maronan Road | HAB | MSL | 98.91999817 | Half arm Barriers with flashing lights and bells |
| Kingdon Street Ped | FLB | NAL | 8.93999958 | Flashing Lights & Bells |
| St Georges Road | FLB | NAL | 18.22999954 | Flashing Lights & Bells |
| ORorke Road | FLB | Onehunga | 0.529999971 | Flashing Lights & Bells |
| Maurice Road | FLB | Onehunga | 0.970000029 | Flashing Lights & Bells |
| Captain Springs Road | FLB | Onehunga | 2.069999933 | Flashing Lights & Bells |
| Church Street | FLB | Onehunga | 2.170000076 | Flashing Lights & Bells |
| Alfred Street | FLB | Onehunga | 2.710000038 | Flashing Lights & Bells |
| Victoria Street | FLB | Onehunga | 2.920000076 | Flashing Lights & Bells |
| Galway Street | FLB | Onehunga | 3.319999933 | Flashing Lights & Bells |
| Church Street East | HAB | NAL | 1.419999957 | Half arm Barriers with flashing lights and bells |
| Normanby Road | HAB | NAL | 10.14999962 | Half arm Barriers with flashing lights and bells |
| Porters Avenue | HAB | NAL | 10.85999966 | Half arm Barriers with flashing lights and bells |
| George Street | HAB | NAL | 11.36999989 | Half arm Barriers with flashing lights and bells |
| Morningside Drive | HAB | NAL | 12.80000019 | Half arm Barriers with flashing lights and bells |
| Asquith Avenue | HAB | NAL | 14.02999973 | Half arm Barriers with flashing lights and bells |
| Rossgrove Terrace | HAB | NAL | 14.13000011 | Half arm Barriers with flashing lights and bells |
| Woodward Road | HAB | NAL | 15.80000019 | Half arm Barriers with flashing lights and bells |
| St Jude Street | HAB | NAL | 17.39999962 | Half arm Barriers with flashing lights and bells |
| Chalmers Street | HAB | NAL | 17.63999939 | Half arm Barriers with flashing lights and bells |
| Sarawia Street | HAB | Newmarket | 0.400000006 | Half arm Barriers with flashing lights and bells |
| Mays Road | HAB | Onehunga | 1.830000043 | Half arm Barriers with flashing lights and bells |
| Queen Street | HAB | SWL |  | Half arm Barriers with flashing lights and bells |
| Dalefield Road | FLB | WL | 73.62000275 | Flashing Lights & Bells |
| Lincoln Road | FLB | WL | 74.80000305 | Flashing Lights & Bells |
| Brooklyn Road | FLB | WL | 75.29000092 | Flashing Lights & Bells |
| Victoria Street | FLB | WL | 76.18000031 | Flashing Lights & Bells |
| Pembroke Street | FLB | WL | 76.44000244 | Flashing Lights & Bells |
| Belvedere Road | FLB | WL | 76.76999664 | Flashing Lights & Bells |
| Rhodes Street | FLB | WL | 77.12000275 | Flashing Lights & Bells |
| Kent Street | FLB | WL | 77.30000305 | Flashing Lights & Bells |
| Chester Road | FLB | WL | 79.44000244 | Flashing Lights & Bells |
| Norman Avenue | FLB | WL | 84.79000092 | Flashing Lights & Bells |
| Norfolk Road | FLB | WL | 85.41999817 | Flashing Lights & Bells |
| Victoria Street | FLB | PNGL | 115.5400009 | Flashing Lights & Bells |
| Tamumu Road | FLB | PNGL | 116.1600037 | Flashing Lights & Bells |
| Racecourse Road | FLB | PNGL | 117.7600021 | Flashing Lights & Bells |
| Higginson Street | FLB | PNGL | 121.8700027 | Flashing Lights & Bells |
| Oruawharo Road | HAB | PNGL | 90.11000061 | Half arm Barriers with flashing lights and bells |
| Fraser Road | HAB | PNGL | 91.47000122 | Half arm Barriers with flashing lights and bells |
| Amyes Road | FLB | Hornby | 0.589999974 | Flashing Lights & Bells |
| Halswell Junction Road | FLB | Hornby | 1.769999981 | Flashing Lights & Bells |
| Wroxton Terrace | FLB | MNL | 2.920000076 | Flashing Lights & Bells |
| Barnes Road | FLB | MNL | 7.829999924 | Flashing Lights & Bells |
| Radcliffe Road | FLB | MNL | 9.520000458 | Flashing Lights & Bells |
| Spencerville Road | FLB | MNL | 13.48999977 | Flashing Lights & Bells |
| Scruttons Road | FLBS | MSL | 5.199999809 | Flashing L & B with Second Train coming |
| Chapmans Road | FLBS | MSL | 5.929999828 | Flashing L & B with Second Train coming |
| Curries Road | FLBS | MSL | 6.75 | Flashing L & B with Second Train coming |
| Riccarton Road | HAB | MNL | 1.480000019 | Half arm Barriers with flashing lights and bells |
| Kilmarnock Street | HAB | MNL | 1.720000029 | Half arm Barriers with flashing lights and bells |
| Fendalton Road | HAB | MNL | 2.49000001 | Half arm Barriers with flashing lights and bells |
| Glandovey Road | HAB | MNL | 3.190000057 | Half arm Barriers with flashing lights and bells |
| Wairakei Road | HAB | MNL | 3.640000105 | Half arm Barriers with flashing lights and bells |
| Blighs Road | HAB | MNL | 4.46999979 | Half arm Barriers with flashing lights and bells |
| Harewood Road | HAB | MNL | 5.159999847 | Half arm Barriers with flashing lights and bells |
| Langdons Road | HAB | MNL | 5.480000019 | Half arm Barriers with flashing lights and bells |
| Sawyers Arms Road | HAB | MNL | 6.099999905 | Half arm Barriers with flashing lights and bells |
| Northcote Road | HAB | MNL | 6.510000229 | Half arm Barriers with flashing lights and bells |
| Tuckers Road | HAB | MNL | 7.039999962 | Half arm Barriers with flashing lights and bells |
| Sturrocks Road | HAB | MNL | 7.559999943 | Half arm Barriers with flashing lights and bells |
| Belfast Road | HAB | MNL | 10.90999985 | Half arm Barriers with flashing lights and bells |
| Factory Road | HAB | MNL | 11.61999989 | Half arm Barriers with flashing lights and bells |
| Marshland Road | HAB | MNL | 13.18999958 | Half arm Barriers with flashing lights and bells |
| Kainga Road | HAB | MNL | 15.19999981 | Half arm Barriers with flashing lights and bells |
| Ensors Road | HAB | MSL | 8.659999847 | Half arm Barriers with flashing lights and bells |
| Wilsons Road | HAB | MSL | 9.279999733 | Half arm Barriers with flashing lights and bells |
| Gasson Street | HAB | MSL | 10.38000011 | Half arm Barriers with flashing lights and bells |
| Montreal Street | HAB | MSL | 11.35999966 | Half arm Barriers with flashing lights and bells |
| Antigua Street | HAB | MSL | 11.57999992 | Half arm Barriers with flashing lights and bells |
| Selwyn Street | HAB | MSL | 12.06999969 | Half arm Barriers with flashing lights and bells |
| Grove Road | HAB | MSL | 12.38000011 | Half arm Barriers with flashing lights and bells |
| Lincoln Road | HAB | MSL | 12.52999973 | Half arm Barriers with flashing lights and bells |
| Whiteleigh Avenue | HAB | MSL | 13.47000027 | Half arm Barriers with flashing lights and bells |
| Matipo Street | HAB | MSL | 14.06999969 | Half arm Barriers with flashing lights and bells |
| Annex Road | HAB | MSL | 15.56999969 | Half arm Barriers with flashing lights and bells |
| Parker Street | HAB | MSL | 20.69000053 | Half arm Barriers with flashing lights and bells |
| Halswell Junction Road | HAB | MSL | 21.27000046 | Half arm Barriers with flashing lights and bells |
| Barters Road | HAB | MSL | 23.23999977 | Half arm Barriers with flashing lights and bells |
| Kirk Road | HAB | MSL | 24.36000061 | Half arm Barriers with flashing lights and bells |
| Dawsons Road | HAB | MSL | 25.85000038 | Half arm Barriers with flashing lights and bells |
| Waihola Place | FLB | MSL | 419.6099854 | Flashing Lights & Bells |
| Benhar Road | FLB | MSL | 454.7000122 | Flashing Lights & Bells |
| Baker Street | FLB | MSL | 458.4299927 | Flashing Lights & Bells |
| High Street | FLB | MSL | 462.5299988 | Flashing Lights & Bells |
| Waiwera Station Road | FLB | MSL | 486.0400085 | Flashing Lights & Bells |
| West Otago Road | FLB | MSL | 511.6400146 | Flashing Lights & Bells |
| Flag Swamp Road | FLB | MSL | 327.1300049 | Flashing Lights & Bells |
| Inverary Street | FLB | MSL | 329.4899902 | Flashing Lights & Bells |
| Beach Street | FLB | MSL | 330.4200134 | Flashing Lights & Bells |
| Coast Road | FLB | MSL | 333.1000061 | Flashing Lights & Bells |
| Coast Road (Puketeraki) | FLB | MSL | 337.8999939 | Flashing Lights & Bells |
| Coast Road (Omimi) | FLB | MSL | 344.230011 | Flashing Lights & Bells |
| Coast Road | FLB | MSL | 345.4899902 | Flashing Lights & Bells |
| Coast Road | FLB | MSL | 346.5100098 | Flashing Lights & Bells |
| Bank Road | FLB | MSL | 347.1199951 | Flashing Lights & Bells |
| Coast Road | FLB | MSL | 347.3699951 | Flashing Lights & Bells |
| Doctors Point Road | FLB | MSL | 354.1700134 | Flashing Lights & Bells |
| Coombe Hay Terrace | FLB | MSL | 366.1000061 | Flashing Lights & Bells |
| Magnet Street | FLB | MSL | 376.9400024 | Flashing Lights & Bells |
| Wharf Street | FLB | MSL |  | Flashing Lights & Bells |
| Riccarton Road | FLB | MSL | 395.2200012 | Flashing Lights & Bells |
| Gladfield Road | FLB | MSL | 397.0299988 | Flashing Lights & Bells |
| Henley-Berwick Road | FLB | MSL | 412.1300049 | Flashing Lights & Bells |
| Wickliffe Terrace | FLB | Port Chalmers | 1.289999962 | Flashing Lights & Bells |
| Gladstone Road | FLB | Taieri | 0.109999999 | Flashing Lights & Bells |
| Factory Road | FLB | Taieri | 1.5 | Flashing Lights & Bells |
| Dukes Road | FLB | Taieri | 2.920000076 | Flashing Lights & Bells |
| Coast Road (Seacliff) | HAB | MSL | 342.6400146 | Half arm Barriers with flashing lights and bells |
| St Andrews Street | HAB | MSL | 378.3399963 | Half arm Barriers with flashing lights and bells |
| Heights Road | FLB | Mission Bush | 2 | Flashing Lights & Bells |
| Patumahoe Road | FLB | Mission Bush | 6.510000229 | Flashing Lights & Bells |
| Pilgrims Road | FLB | Mission Bush | 10.01000023 | Flashing Lights & Bells |
| Sommerville Road | FLB | Mission Bush | 10.97000027 | Flashing Lights & Bells |
| Glenbrook Station Road | FLB | Mission Bush | 11.59000015 | Flashing Lights & Bells |
| Kellyville Road | HAB | NIMT | 610.5100098 | Half arm Barriers with flashing lights and bells |
| McDonald Road | HAB | NIMT | 613.2000122 | Half arm Barriers with flashing lights and bells |
| Harrisville Road | HAB | NIMT | 621.6099854 | Half arm Barriers with flashing lights and bells |
| Logan Road | HAB | NIMT | 625.6799927 | Half arm Barriers with flashing lights and bells |
| Crown Road | HAB | NIMT | 633.5700073 | Half arm Barriers with flashing lights and bells |
| Lytton Road | FLB | PNGL | 387.7399902 | Flashing Lights & Bells |
| Stanley Road | FLB | PNGL | 388.9500122 | Flashing Lights & Bells |
| Grey Street | FLB | PNGL | 390.2000122 | Flashing Lights & Bells |
| Ontario Street | FLB | MSL | 537 | Flashing Lights & Bells |
| River Street | FLB | MSL | 537.289978 | Flashing Lights & Bells |
| Mersey Street | FLB | MSL | 537.5800171 | Flashing Lights & Bells |
| Hyde Street | FLB | MSL | 538.1300049 | Flashing Lights & Bells |
| Bury Street | FLB | MSL | 538.6199951 | Flashing Lights & Bells |
| Salford Street | FLB | MSL | 539.2299805 | Flashing Lights & Bells |
| Selbourne Street | FLB | MSL | 548 | Flashing Lights & Bells |
| Albion Street | FLB | MSL | 550.2299805 | Flashing Lights & Bells |
| Rayonier Crossing | FLB | MSL | 553.8200073 | Flashing Lights & Bells |
| Nelson Street | FLB | Hokitika | 2.779999971 | Flashing Lights & Bells |
| Weenink Road | FLB | Hokitika | 3.349999905 | Flashing Lights & Bells |
| Arnold Valley Road | FLB | Midland | 178.4299927 | Flashing Lights & Bells |
| Blair Road | FLB | Midland | 191.0599976 | Flashing Lights & Bells |
| Taupo Terrace | FLB | Midland | 202.3000031 | Flashing Lights & Bells |
| Mawhera Quay | FLB | Midland | 210.8200073 | Flashing Lights & Bells |
| Albert Street | FLB | Midland | 211.3899994 | Flashing Lights & Bells |
| Tarapuhi Street | FLB | Midland | 211.5 | Flashing Lights & Bells |
| Herbert Street | FLB | Midland | 211.6499939 | Flashing Lights & Bells |
| Tainui Street | HAB | Midland | 211.2700043 | Half arm Barriers with flashing lights and bells |
| Grey Street | HAB | ECMT | 2.730000019 | Half arm Barriers with flashing lights and bells |
| Peachgrove Road | HAB | ECMT | 3.700000048 | Half arm Barriers with flashing lights and bells |
| Killarney Road | HAB | NIMT | 541.4400024 | Half arm Barriers with flashing lights and bells |
| Te Kowhai Road | HAB | NIMT | 548.0999756 | Half arm Barriers with flashing lights and bells |
| Ruffell Road | HAB | NIMT | 549.7999878 | Half arm Barriers with flashing lights and bells |
| Te Aute Trust Road | FLB | PNGL | 134.6000061 | Flashing Lights & Bells |
| Poukawa Crossing | FLB | PNGL | 141.9600067 | Flashing Lights & Bells |
| Te Mahunga Road | FLB | PNGL | 145.1900024 | Flashing Lights & Bells |
| Stock Road | FLB | PNGL | 151.2899933 | Flashing Lights & Bells |
| Te Aute Road | FLB | PNGL | 152.0099945 | Flashing Lights & Bells |
| Longlands Road | FLB | PNGL | 155.2899933 | Flashing Lights & Bells |
| Davis Road | FLB | PNGL | 155.8699951 | Flashing Lights & Bells |
| Anderson Road | FLB | PNGL |  | Flashing Lights & Bells |
| Tollemache Road | HAB | PNGL | 157.0299988 | Half arm Barriers with flashing lights and bells |
| Murdoch Road | HAB | PNGL | 157.6399994 | Half arm Barriers with flashing lights and bells |
| Lyndon Road | HAB | PNGL | 158.8000031 | Half arm Barriers with flashing lights and bells |
| Eastbourne Street | HAB | PNGL | 158.9199982 | Half arm Barriers with flashing lights and bells |
| Queen Street | HAB | PNGL | 159.1600037 | Half arm Barriers with flashing lights and bells |
| St Aubyn Street | HAB | PNGL | 159.4100037 | Half arm Barriers with flashing lights and bells |
| Frederick Street | HAB | PNGL | 160.4499969 | Half arm Barriers with flashing lights and bells |
| Ellwood Road | HAB | PNGL | 162.0700073 | Half arm Barriers with flashing lights and bells |
| Ruahapia Road | HAB | PNGL | 163.4100037 | Half arm Barriers with flashing lights and bells |
| Whakatu Road | HAB | PNGL | 164.0599976 | Half arm Barriers with flashing lights and bells |
| South Manakau Road | FLB | NIMT | 77.55999756 | Flashing Lights & Bells |
| North Manakau Road | FLB | NIMT | 80.56999969 | Flashing Lights & Bells |
| Kuku Beach Road | FLB | NIMT | 83.73000336 | Flashing Lights & Bells |
| McLeavey Road | FLB | NIMT | 87.19999695 | Flashing Lights & Bells |
| Roslyn Road | FLB | NIMT | 93.18000031 | Flashing Lights & Bells |
| Heatherlea East Road | FLB | NIMT | 95.41000366 | Flashing Lights & Bells |
| Tavistock Road | FLB | NIMT | 98.79000092 | Flashing Lights & Bells |
| Vance Street | FLB | NIMT | 106.4100037 | Flashing Lights & Bells |
| Okuku Road | FLB | NIMT | 110.0199966 | Flashing Lights & Bells |
| Mokena Kohere Street | HAB | NIMT | 79.56999969 | Half arm Barriers with flashing lights and bells |
| Tararua Road | HAB | NIMT | 89.62000275 | Half arm Barriers with flashing lights and bells |
| Mako Mako Road | HAB | NIMT | 90.63999939 | Half arm Barriers with flashing lights and bells |
| Bath Street | HAB | NIMT | 91.33000183 | Half arm Barriers with flashing lights and bells |
| Queen Street | HAB | NIMT | 91.58999634 | Half arm Barriers with flashing lights and bells |
| Tyne Street | HAB | NIMT | 92.31999969 | Half arm Barriers with flashing lights and bells |
| Sheehan Street | HAB | NIMT | 106.9100037 | Half arm Barriers with flashing lights and bells |
| Douglas Road | FLB | MNL | 51.75 | Flashing Lights & Bells |
| Georges Road | FLB | MNL | 60.29000092 | Flashing Lights & Bells |
| Johnston Street | FLB | MNL | 63.25 | Flashing Lights & Bells |
| Church Road | FLB | MNL | 64.12999725 | Flashing Lights & Bells |
| Scargill Valley Road | HAB | MNL | 86.30000305 | Half arm Barriers with flashing lights and bells |
| Manor Park Road | HAB | WL | 23.19000053 | Half arm Barriers with flashing lights and bells |
| Parkside Road | HAO | Gracefield | 1.820000052 | Half arm Barriers Out of use |
| Hutt Park Road | HAO | Gracefield | 2.319999933 | Half arm Barriers Out of use |
| Ettrick Street | FLB | Bluff | 0.769999981 | Flashing Lights & Bells |
| Crinan Street | FLB | Bluff | 1.029999971 | Flashing Lights & Bells |
| Bond Street | FLB | Bluff | 1.379999995 | Flashing Lights & Bells |
| Rimu Road | FLB | MSL | 592.5999756 | Flashing Lights & Bells |
| Mill Road South | FLB | MSL | 594.960022 | Flashing Lights & Bells |
| Inglewood Road | FLB | MSL | 598.1300049 | Flashing Lights & Bells |
| Conon Street | FLB | MSL | 600.4000244 | Flashing Lights & Bells |
| Nith Street | FLB | MSL | 600.6400146 | Flashing Lights & Bells |
| Heywood Street | FLB | Ohai | 3.150000095 | Flashing Lights & Bells |
| Renfrew Street | FLB | Ohai | 3.799999952 | Flashing Lights & Bells |
| Durham Street | FLB | Ohai | 4.079999924 | Flashing Lights & Bells |
| West Plains Road | FLB | Ohai | 4.760000229 | Flashing Lights & Bells |
| Moore Road | FLB | Ohai | 5.980000019 | Flashing Lights & Bells |
| Steel Road | FLB | Ohai |  | Flashing Lights & Bells |
| Lindisfarne Street | HAB | MSL | 598.9299927 | Half arm Barriers with flashing lights and bells |
| Elles Road | HAB | MSL | 599.8099976 | Half arm Barriers with flashing lights and bells |
| Ythan Street | HAB | MSL | 600.1599731 | Half arm Barriers with flashing lights and bells |
| Liddel Street | HAB | MSL | 601.039978 | Half arm Barriers with flashing lights and bells |
| Victoria Avenue | HAB | Ohai | 0.699999988 | Half arm Barriers with flashing lights and bells |
| Bay Road | HAB | Ohai | 2.579999924 | Half arm Barriers with flashing lights and bells |
| Inland Kaikoura Road | FLB | MNL | 184.2400055 | Flashing Lights & Bells |
| Oruawharo Road | FLB | NAL | 131.5800018 | Flashing Lights & Bells |
| Oneriri Road | FLB | NAL | 138.8600006 | Flashing Lights & Bells |
| Whakapirau Road | FLB | NAL | 149.9299927 | Flashing Lights & Bells |
| Waterfall Road | FLB | NIMT | 43.61999893 | Flashing Lights & Bells |
| Hadfield Road | FLB | NIMT | 59.93999863 | Flashing Lights & Bells |
| School Road | FLB | NIMT | 65.11000061 | Flashing Lights & Bells |
| Old Hautere Road | FLB | NIMT | 67.55000305 | Flashing Lights & Bells |
| Rahui Road | FLB | NIMT | 70.79000092 | Flashing Lights & Bells |
| Beach Road | HAB | NIMT | 38.61999893 | Half arm Barriers with flashing lights and bells |
| Kapiti Road | HAB | NIMT | 48.38000107 | Half arm Barriers with flashing lights and bells |
| Otaihanga Road | HAB | NIMT | 51.61000061 | Half arm Barriers with flashing lights and bells |
| Elizabeth Street | HAB | NIMT | 55.25999832 | Half arm Barriers with flashing lights and bells |
| Reserve Road | FLB | NIMT | 130.4400024 | Flashing Lights & Bells |
| Cloverlea Road | FLB | NIMT | 133.4299927 | Flashing Lights & Bells |
| Roberts Line | FLB | NIMT | 141.5399933 | Flashing Lights & Bells |
| Clevely Line | FLB | NIMT | 143.8099976 | Flashing Lights & Bells |
| Makino Road | FLB | NIMT | 156.0599976 | Flashing Lights & Bells |
| Lethbridge Road | FLB | NIMT | 158.6699982 | Flashing Lights & Bells |
| Godley Street | FLB | NIMT | 166.6900024 | Flashing Lights & Bells |
| Kairanga-Bunnythorpe Road | HAB | NIMT | 144.8300018 | Half arm Barriers with flashing lights and bells |
| Newbury Line | HAB | NIMT | 146.7100067 | Half arm Barriers with flashing lights and bells |
| Aorangi Works Road | HAB | NIMT | 151.1000061 | Half arm Barriers with flashing lights and bells |
| East Street | HAB | NIMT | 152.1300049 | Half arm Barriers with flashing lights and bells |
| Grey Street | HAB | NIMT | 153.5399933 | Half arm Barriers with flashing lights and bells |
| North Street | HAB | NIMT | 154.5599976 | Half arm Barriers with flashing lights and bells |
| Monteith Street | HAB | NIMT | 165.5500031 | Half arm Barriers with flashing lights and bells |
| Stanway Road | HAB | NIMT | 166.0200043 | Half arm Barriers with flashing lights and bells |
| Homai South Ped | FLB | NIMT | 655.6199951 | Flashing Lights & Bells |
| Homai North Ped | FLB | NIMT | 655.7700195 | Flashing Lights & Bells |
| Papatoetoe Up Ped | FLB | NIMT | 660.4400024 | Flashing Lights & Bells |
| Papatoetoe Down Ped | FLB | NIMT | 660.4500122 | Flashing Lights & Bells |
| Dalgety Drive | FLO | NIMT |  | Out of use |
| Alabama Road | FLB | MNL | 316.6199951 | Flashing Lights & Bells |
| Stuart Street | FLB | MNL | 318.1199951 | Flashing Lights & Bells |
| Kinross Street | FLB | MNL | 318.5700073 | Flashing Lights & Bells |
| Horton Street | FLB | MNL | 319.0899963 | Flashing Lights & Bells |
| Lower Wairau Road | FLB | MNL | 320.8500061 | Flashing Lights & Bells |
| Aberharts Road | FLB | MNL | 321.1700134 | Flashing Lights & Bells |
| Fell Street | FLB | MNL | 322.3500061 | Flashing Lights & Bells |
| Ferry Road | FLB | MNL | 324.7999878 | Flashing Lights & Bells |
| Hunters Road | FLB | MNL | 328.230011 | Flashing Lights & Bells |
| Lagoon Road | FLB | MNL |  | Flashing Lights & Bells |
| Cloudy Bay Drive | HAB | MNL | 312.1600037 | Half arm Barriers with flashing lights and bells |
| Dillons Point Road | HAB | MNL | 319.3800049 | Half arm Barriers with flashing lights and bells |
| Budge Street | HAB | MNL | 319.9200134 | Half arm Barriers with flashing lights and bells |
| Dublin Street | HAB | MNL | 347.3500061 | Half arm Barriers with flashing lights and bells |
| Judds Road | FLB | WL | 87.84999847 | Flashing Lights & Bells |
| Hillcrest Street | FLB | WL | 88.36000061 | Flashing Lights & Bells |
| Cornwall Street | FLB | WL | 88.93000031 | Flashing Lights & Bells |
| Renall Street | FLB | WL | 89.48999786 | Flashing Lights & Bells |
| Akura Road | FLB | WL | 91.16000366 | Flashing Lights & Bells |
| Opaki-Kaiparoro Road | FLB | WL | 98.40000153 | Flashing Lights & Bells |
| Opaki-Kaiparoro Road | FLB | WL | 101.6800003 | Flashing Lights & Bells |
| Opaki-Kaiparoro Road | FLB | WL | 106.7600021 | Flashing Lights & Bells |
| Opaki-Kaiparoro Road | FLB | WL | 111.2099991 | Flashing Lights & Bells |
| Ngaumutawa Road | HAB | WL | 86.90000153 | Half arm Barriers with flashing lights and bells |
| Boltons Road | FLB | ECMT | 32.20000076 | Flashing Lights & Bells |
| Kiwitahi Station Road | FLB | ECMT | 37.97999954 | Flashing Lights & Bells |
| Hutchinson Road | FLB | ECMT | 43.54999924 | Flashing Lights & Bells |
| Puketutu Road | FLB | Kinleith | 12.36999989 | Flashing Lights & Bells |
| Morrinsville-Walton Road | FLO | ECMT |  | Out of use |
| Avenue Road | HAB | ECMT | 27.70999908 | Half arm Barriers with flashing lights and bells |
| Lorne Street | HAB | ECMT | 28.62000084 | Half arm Barriers with flashing lights and bells |
| Kereone Road | HAB | ECMT | 30.55999947 | Half arm Barriers with flashing lights and bells |
| Hawes Street | HAB | Kinleith | 1.169999957 | Half arm Barriers with flashing lights and bells |
| Pohlen Road | HAB | Kinleith | 4.539999962 | Half arm Barriers with flashing lights and bells |
| Tainui Street | HAB | Kinleith | 7.949999809 | Half arm Barriers with flashing lights and bells |
| Lever Street | FLB | Napier | 1.970000029 | Flashing Lights & Bells |
| Waghorne Street | FLB | Napier | 3.25999999 | Flashing Lights & Bells |
| Hastings Street | FLB | PNGL | 177.3000031 | Flashing Lights & Bells |
| Owen Street | FLB | PNGL | 178.5899963 | Flashing Lights & Bells |
| Jull Street | FLB | PNGL | 178.8300018 | Flashing Lights & Bells |
| Severn Street | FLB | PNGL | 180.6999969 | Flashing Lights & Bells |
| Domain Road | FLB | PNGL | 183.9900055 | Flashing Lights & Bells |
| Waitangi Road | HAB | PNGL | 171.2400055 | Half arm Barriers with flashing lights and bells |
| Awatoto Road | HAB | PNGL | 173.4700012 | Half arm Barriers with flashing lights and bells |
| Sale Street | HAB | PNGL | 177.6900024 | Half arm Barriers with flashing lights and bells |
| Raffles Street | HAB | PNGL | 177.9900055 | Half arm Barriers with flashing lights and bells |
| Dickens Street | HAB | PNGL | 178.3999939 | Half arm Barriers with flashing lights and bells |
| Prebensen Drive | HAB | PNGL | 180.0299988 | Half arm Barriers with flashing lights and bells |
| Old Mountain Road | FLB | MNPL | 174.0500031 | Flashing Lights & Bells |
| Surrey Road | FLB | MNPL | 174.3399963 | Flashing Lights & Bells |
| Norfolk Road | FLB | MNPL | 178.2400055 | Flashing Lights & Bells |
| Durham Road | FLB | MNPL | 180.3399963 | Flashing Lights & Bells |
| Dudley Road | FLB | MNPL | 182.5800018 | Flashing Lights & Bells |
| Standish Street | FLB | MNPL | 183.2400055 | Flashing Lights & Bells |
| Carrington Street | FLB | MNPL | 183.8099976 | Flashing Lights & Bells |
| Humphries Street | FLB | MNPL | 184.0700073 | Flashing Lights & Bells |
| Hursthouse Road | FLB | MNPL | 184.9199982 | Flashing Lights & Bells |
| Manutahi Road | FLB | MNPL | 194.4299927 | Flashing Lights & Bells |
| Corbett Road | FLB | MNPL | 199.6600037 | Flashing Lights & Bells |
| Paraite Road | FLB | MNPL | 201.0899963 | Flashing Lights & Bells |
| Henwood Road | FLB | MNPL | 202.0099945 | Flashing Lights & Bells |
| Queens Road | FLB | MNPL | 205.4499969 | Flashing Lights & Bells |
| Bulkeley Terrace | FLB | MNPL | 209.6300049 | Flashing Lights & Bells |
| Belt Road | FLB | MNPL | 210.25 | Flashing Lights & Bells |
| Bayly Road | FLB | MNPL | 211.5299988 | Flashing Lights & Bells |
| SH 16 | FLB | NAL | 74.62999725 | Flashing Lights & Bells |
| SH 30 | FLB | ECMT | 177.4199982 | Flashing Lights & Bells |
| Kawerau Road (SH 34) | FLB | Murupara | 0.310000002 | Flashing Lights & Bells |
| Hewletts Rd AKZO Nobel | FLO | Mt Maunganui | Out of use |
| SH 30 | FLO | Taneatua | 12.05000019 | Out of use |
| White Pine Bush Rd (SH 2) | FLO | Whakatane | 0.889999986 | Out of use |
| SH 2 | HAB | ECMT | 104.4100037 | Half arm Barriers with flashing lights and bells |
| SH 2 | HAB | ECMT | 127.4100037 | Half arm Barriers with flashing lights and bells |
| Hewletts Road (SH 29) | HAB | Mt Maunganui | 2.720000029 | Half arm Barriers with flashing lights and bells |
| Essendon Road (SH 73) | FLB | Midland | 18.84000015 | Flashing Lights & Bells |
| SH 1 | FLB | MNL | 73.40000153 | Flashing Lights & Bells |
| SH 1 | FLB | MSL | 74.73999786 | Flashing Lights & Bells |
| SH 79 | FLB | MSL | 130.8699951 | Flashing Lights & Bells |
| SH 1 (Winchester) | FLB | MSL | 144.4799957 | Flashing Lights & Bells |
| Main South Road (SH 73) | HAB | Hornby | 0.379999995 | Half arm Barriers with flashing lights and bells |
| Lineside Road (SH 71) | HAB | MNL | 26.54000092 | Half arm Barriers with flashing lights and bells |
| Waipara Flat Road (SH 7) | HAB | MNL | 61.95999908 | Half arm Barriers with flashing lights and bells |
| SH 1 | HAB | MNL | 77.93000031 | Half arm Barriers with flashing lights and bells |
| Garlands Road (SH 74A) | HAB | MSL | 7.409999847 | Half arm Barriers with flashing lights and bells |
| Carmen Road (SH 1) | HAB | MSL | 19.75 | Half arm Barriers with flashing lights and bells |
| SH 1 (Selwyn) | HAB | MSL | 47.02000046 | Half arm Barriers with flashing lights and bells |
| Kermode Street (SH 1) | HAB | MSL | 95.56999969 | Half arm Barriers with flashing lights and bells |
| Awapuni Road (SH 35) | FLB | PNGL | 385.3900146 | Flashing Lights & Bells |
| Customhouse St (SH 35) | FLB | PNGL | 390.7200012 | Flashing Lights & Bells |
| Breakwater Road (SH 50) | FLB | Napier |  | Flashing Lights & Bells |
| SH 2 (Meeanee Quay) | FLB | PNGL | 183.4299927 | Flashing Lights & Bells |
| Carroll Street (SH 38) | FLB | PNGL | 294.7399902 | Flashing Lights & Bells |
| Te Uhi Road (SH 2) | FLB | PNGL | 296.75 | Flashing Lights & Bells |
| Pandora Road (SH 2) | HAB | Napier | 1.029999971 | Half arm Barriers with flashing lights and bells |
| Bridge Street (SH 50) | HAB | Napier | 2.289999962 | Half arm Barriers with flashing lights and bells |
| Breakwater Road (SH 50) | HAB | Napier | 3.380000114 | Half arm Barriers with flashing lights and bells |
| Ruataniwha Street (SH 2) | HAB | PNGL | 108.2300034 | Half arm Barriers with flashing lights and bells |
| Southampton Street (SH 2) | HAB | PNGL | 158.6699982 | Half arm Barriers with flashing lights and bells |
| Ellison Street (SH 2) | HAB | PNGL | 176.4100037 | Half arm Barriers with flashing lights and bells |
| Georges Drive (SH 2) | HAB | PNGL | 179.3300018 | Half arm Barriers with flashing lights and bells |
| Taradale Road (SH 50) | HAB | PNGL | 179.8500061 | Half arm Barriers with flashing lights and bells |
| SH 1 (Onslow Street) | FLB | NIMT | 221.9400024 | Flashing Lights & Bells |
| SH 49 | FLB | NIMT | 299.8800049 | Flashing Lights & Bells |
| SH 2 | FLB | PNGL | 49.33000183 | Flashing Lights & Bells |
| McLean Street (SH 2) | FLB | WL | 170.3800049 | Flashing Lights & Bells |
| Kimberley Road (SH 57) | HAB | NIMT | 87.93000031 | Half arm Barriers with flashing lights and bells |
| Opiki Road (SH 56) | HAB | NIMT | 111.7699966 | Half arm Barriers with flashing lights and bells |
| Kimbolton Road (SH 54) | HAB | NIMT | 153.1300049 | Half arm Barriers with flashing lights and bells |
| SH 1 | HAB | NIMT | 231.2299957 | Half arm Barriers with flashing lights and bells |
| McLean Street (SH 2) | HAB | PNGL | 26.93000031 | Half arm Barriers with flashing lights and bells |
| Wairau Road (SH 1) | FLB | MNL | 347.0799866 | Flashing Lights & Bells |
| Main Street (SH 1) | HAB | MNL | 318.7799988 | Half arm Barriers with flashing lights and bells |
| SH 1 | FLB | NAL | 243.2100067 | Flashing Lights & Bells |
| SH 1 | FLB | NAL | 251.8899994 | Flashing Lights & Bells |
| SH 1 Kamo | HAB | NAL | 218.1300049 | Half arm Barriers with flashing lights and bells |
| SH 1 | FLB | MSL | 267.8099976 | Flashing Lights & Bells |
| Beach Street (SH 88) | FLB | Port Chalmers | 1.74000001 | Flashing Lights & Bells |
| Severn Street (SH 1) | HAB | MSL | 255 | Half arm Barriers with flashing lights and bells |
| Gordon Road (SH 87) | HAB | MSL | 393.3900146 | Half arm Barriers with flashing lights and bells |
| Main Road (SH 1) | HAB | MSL | 495.7200012 | Half arm Barriers with flashing lights and bells |
| SH 1 | FL | Bluff |  | Flashing Lights |
| SH 1 | FLB | Bluff |  | Flashing Lights & Bells |
| Bridge Street (SH 93) | FLB | MSL | 549.6699829 | Flashing Lights & Bells |
| SH 1 | FLB | MSL |  | Flashing Lights & Bells |
| Clyde Street (SH 1) | HAB | MSL | 600.8800049 | Half arm Barriers with flashing lights and bells |
| SH 43 (Toko) | FLB | SOL | 9.539999962 | Flashing Lights & Bells |
| SH 43 (Near Gordons Road) | FLB | SOL | 13.46000004 | Flashing Lights & Bells |
| SH 43 (Douglas) | FLB | SOL | 17.64999962 | Flashing Lights & Bells |
| Regan Street (SH 43) | HAB | MNPL | 162.2599945 | Half arm Barriers with flashing lights and bells |
| Rata Street (SH 3A) | HAB | MNPL | 183.5599976 | Half arm Barriers with flashing lights and bells |
| SH 26 | FLB | Cambridge | 2.720000029 | Flashing Lights & Bells |
| SH 26 (Piako Road) | FLB | ECMT | 24.54999924 | Flashing Lights & Bells |
| Bennydale Road (SH 30) | FLB | NIMT | 449.7399902 | Flashing Lights & Bells |
| SH 27 | FLB | Waitoa | 7.260000229 | Flashing Lights & Bells |
| SH 27 | HAB | Kinleith | 2.130000114 | Half arm Barriers with flashing lights and bells |
| Broadway (SH 24) | HAB | Kinleith | 7.300000191 | Half arm Barriers with flashing lights and bells |
| Burwood Road (SH 27) | HAB | Kinleith | 9.199999809 | Half arm Barriers with flashing lights and bells |
| SH 29 | HAB | Kinleith | 15.73999977 | Half arm Barriers with flashing lights and bells |
| Awakino Road (SH 30) | HAB | NIMT | 475.4500122 | Half arm Barriers with flashing lights and bells |
| Kahikatea Drive (SH 1) | HAB | NIMT | 540.1199951 | Half arm Barriers with flashing lights and bells |
| Ellery Street (SH 39) | HAB | NIMT | 558.7399902 | Half arm Barriers with flashing lights and bells |
| Huntly Bypass (SH 1) | HAB | Rotowaro | 0.07 | Half arm Barriers with flashing lights and bells |
| McKays Crossing | HAB | NIMT | 41.79000092 | Half arm Barriers with flashing lights and bells |
| Revans Street (SH 53) | HAB | WL | 56.45999908 | Half arm Barriers with flashing lights and bells |
| Fitzherbert Street (SH 2) | HAB | WL | 56.52999878 | Half arm Barriers with flashing lights and bells |
| SH 6 | FLB | Hokitika | 17.45999908 | Flashing Lights & Bells |
| Aickens (SH 73) | FLB | Midland | 138.1499939 | Flashing Lights & Bells |
| SH 73 | FLB | Midland | 140.6799927 | Flashing Lights & Bells |
| SH 6 (Seven Mile Road) | FLB | Rapahoe | 6.380000114 | Flashing Lights & Bells |
| SH 7 Raupo | FLB | SWL | 25.72999954 | Flashing Lights & Bells |
| SH 7 (Dudleys) | FLB | SWL | 30.07999992 | Flashing Lights & Bells |
| SH 7 (Hinau) | FLB | SWL | 48.25999832 | Flashing Lights & Bells |
| Buller Road (SH 69) | FLB | SWL | 61.06999969 | Flashing Lights & Bells |
| SH 69 (Landing Bridge) | FLB | SWL | 84.76000214 | Flashing Lights & Bells |
| SH 69 Oweka | FLB | SWL | 89.79000092 | Flashing Lights & Bells |
| SH 67 | FLB | SWL | 143.8099976 | Flashing Lights & Bells |
| SH 67 Granity | FLB | SWL | 160.9900055 | Flashing Lights & Bells |
| SH 67 | HAB | SWL |  | Half arm Barriers with flashing lights and bells |
| Kio Kio Station Road | FLB | NIMT | 498.8299866 | Flashing Lights & Bells |
| Te Kawa Road | HAB | NIMT | 506.6799927 | Half arm Barriers with flashing lights and bells |
| Tane Road | FLB | NIMT | 120.4100037 | Flashing Lights & Bells |
| Akers Road | FLB | NIMT | 124.5999985 | Flashing Lights & Bells |
| James Line | FLB | PNGL | 5.159999847 | Flashing Lights & Bells |
| Stoney Creek Road | FLB | PNGL | 6.21999979 | Flashing Lights & Bells |
| Tremaine Avenue | HAB | PNGL | 1.860000014 | Half arm Barriers with flashing lights and bells |
| Roberts Line | HAB | PNGL | 4.159999847 | Half arm Barriers with flashing lights and bells |
| Sutton Road | HAB | NIMT | 643.3599854 | Half arm Barriers with flashing lights and bells |
| Opaheke Road | HAB | NIMT | 644.5999756 | Half arm Barriers with flashing lights and bells |
| Boundary Road | HAB | NIMT | 645.5300293 | Half arm Barriers with flashing lights and bells |
| Walters Road | HAB | NIMT | 649.1900024 | Half arm Barriers with flashing lights and bells |
| Taka Street | HAB | NIMT | 650.3800049 | Half arm Barriers with flashing lights and bells |
| Manuroa Road | HAB | NIMT | 650.8900146 | Half arm Barriers with flashing lights and bells |
| Spartan Road | HAB | NIMT | 651.460022 | Half arm Barriers with flashing lights and bells |
| Pascoe Avenue | HAB | NIMT | 22.88999939 | Half arm Barriers with flashing lights and bells |
| Steyne Avenue | HAB | NIMT | 24.15999985 | Half arm Barriers with flashing lights and bells |
| Pukepapa Road | FLB | MNPL | 2.079999924 | Flashing Lights & Bells |
| Makirikiri Road | FLB | NIMT | 178.2400055 | Flashing Lights & Bells |
| Station Road | FLB | NIMT | 180.5299988 | Flashing Lights & Bells |
| Porewa Road | FLB | NIMT | 190.7599945 | Flashing Lights & Bells |
| Putorino Road | FLB | NIMT | 196.1999969 | Flashing Lights & Bells |
| Main Street | FLB | NIMT | 204.7599945 | Flashing Lights & Bells |
| High Street | FLB | NIMT | 205.0500031 | Flashing Lights & Bells |
| Otara Road | FLB | NIMT | 222.9499969 | Flashing Lights & Bells |
| Toetoe Road | FLB | NIMT | 241.8300018 | Flashing Lights & Bells |
| Utiku North Road | FLB | NIMT | 243.9600067 | Flashing Lights & Bells |
| Gorge Road | FLB | NIMT | 245.6000061 | Flashing Lights & Bells |
| Rauma Road | FLB | NIMT | 250.3300018 | Flashing Lights & Bells |
| Ruru Road | FLB | NIMT | 253.0500031 | Flashing Lights & Bells |
| King Street | HAB | MNPL | 0.170000002 | Half arm Barriers with flashing lights and bells |
| Matai Street | HAB | NIMT | 180.8600006 | Half arm Barriers with flashing lights and bells |
| Taupaki Road | FLB | NAL | 39.43000031 | Flashing Lights & Bells |
| Access Road | FLB | NAL | 44.5 | Flashing Lights & Bells |
| Waimauku Station Road | FLB | NAL | 50.77000046 | Flashing Lights & Bells |
| Kanohi Road | FLB | NAL | 77.69000244 | Flashing Lights & Bells |
| Silver Hill Road | FLB | NAL | 124.6200027 | Flashing Lights & Bells |
| Maraeroa Road | FLO | Rotorua | 29.23999977 | Out of use |
| Ngongotaha Road | FLO | Rotorua | 42.04999924 | Out of use |
| Taui Street | FLO | Rotorua | 42.66999817 | Out of use |
| Kawaha Point Road | HAO | Rotorua | 46.40999985 | Half arm Barriers Out of use |
| Fisher Road | FLB | NIMT | 347.2600098 | Flashing Lights & Bells |
| Oio Road | FLB | NIMT | 371.1400146 | Flashing Lights & Bells |
| Kawautahi Road | FLB | NIMT | 372.3900146 | Flashing Lights & Bells |
| Owhango Road | FLB | NIMT | 372.7200012 | Flashing Lights & Bells |
| Service Road | FLB | NIMT | 381.3699951 | Flashing Lights & Bells |
| Racecourse Road | FLB | NIMT | 393.75 | Flashing Lights & Bells |
| Ongarue Back Road | FLB | NIMT | 402.2200012 | Flashing Lights & Bells |
| Ongarue Back Road | FLB | NIMT | 410.6600037 | Flashing Lights & Bells |
| Porootarao Road | FLB | NIMT | 434.5599976 | Flashing Lights & Bells |
| Ngauruhoe Street | HAB | NIMT | 290.6300049 | Half arm Barriers with flashing lights and bells |
| Raurimu Road | HAB | NIMT | 358.8200073 | Half arm Barriers with flashing lights and bells |
| Titoki Street | HAB | NIMT | 391.5400085 | Half arm Barriers with flashing lights and bells |
| Ongarue Village Road | HAB | NIMT | 420.4200134 | Half arm Barriers with flashing lights and bells |
| Jones Road | FLB | Midland | 0.660000026 | Flashing Lights & Bells |
| Bealey Road | FLB | Midland | 11.39000034 | Flashing Lights & Bells |
| Horndon Street | FLB | Midland | 23.53000069 | Flashing Lights & Bells |
| Mathias Street | FLB | Midland | 24.77000046 | Flashing Lights & Bells |
| McMillan Street | FLB | Midland | 25.48999977 | Flashing Lights & Bells |
| North Terrace | FLB | Midland | 26.12000084 | Flashing Lights & Bells |
| Waimakariri Gorge Road | FLB | Midland | 37.27000046 | Flashing Lights & Bells |
| Curve Road | FLB | Midland | 38.34000015 | Flashing Lights & Bells |
| Queen Street | FLB | Midland | 39.36999893 | Flashing Lights & Bells |
| Aylesbury Road | FLB | MSL | 38.91999817 | Flashing Lights & Bells |
| Telegraph Road | FLB | MSL | 45.11000061 | Flashing Lights & Bells |
| Boundary Creek Road | FLB | MSL | 48.84999847 | Flashing Lights & Bells |
| Browns Road | FLB | MSL | 49.97000122 | Flashing Lights & Bells |
| Pococks Road | HAB | Midland | 48.74000168 | Half arm Barriers with flashing lights and bells |
| Curraghs Road | HAB | MSL | 27.17000008 | Half arm Barriers with flashing lights and bells |
| Weedons Ross Road | HAB | MSL | 30.32999992 | Half arm Barriers with flashing lights and bells |
| Hoskyns Road | HAB | MSL | 32.43000031 | Half arm Barriers with flashing lights and bells |
| Mount White Bridge | PB | Midland | 96.08000183 | Level Xing with bells only |
| Palmer Road | FLB | Kapuni | 8.300000191 | Flashing Lights & Bells |
| Lower Okotuku Road | FLB | MNPL | 85.62000275 | Flashing Lights & Bells |
| Oturi Road | FLB | MNPL | 89.73000336 | Flashing Lights & Bells |
| Mokoia Road | FLB | MNPL | 122.8899994 | Flashing Lights & Bells |
| Whareroa Road | FLB | MNPL | 129.8999939 | Flashing Lights & Bells |
| High Street | FLB | MNPL | 132.0299988 | Flashing Lights & Bells |
| Tawhiti Road | FLB | MNPL | 132.7400055 | Flashing Lights & Bells |
| Turuturu Road | FLB | MNPL | 134.1499939 | Flashing Lights & Bells |
| Ohangai Road | FLB | MNPL | 137.0599976 | Flashing Lights & Bells |
| Egmont Street | FLB | MNPL | 137.9499969 | Flashing Lights & Bells |
| Austin Road | FLB | MNPL | 140.2899933 | Flashing Lights & Bells |
| London Street | FLB | MNPL | 151.4600067 | Flashing Lights & Bells |
| Bridge Street | FLB | MNPL | 151.6199951 | Flashing Lights & Bells |
| George Street | FLB | MNPL | 152.3000031 | Flashing Lights & Bells |
| Clifford Road | FLB | MNPL | 152.6600037 | Flashing Lights & Bells |
| Rangipai Road | FLB | Kinleith | 21.01000023 | Flashing Lights & Bells |
| Totman Road | FLB | Kinleith | 22.59000015 | Flashing Lights & Bells |
| Kinloch Road | FLB | Kinleith | 42.65999985 | Flashing Lights & Bells |
| Vospers Road | FLB | Kinleith | 43.77000046 | Flashing Lights & Bells |
| Rollett Road | FLB | Kinleith | 54.59000015 | Flashing Lights & Bells |
| Baird Road | FLB | Kinleith | 56.50999832 | Flashing Lights & Bells |
| Bridge Street | FLB | Kinleith | 57.34999847 | Flashing Lights & Bells |
| Balmoral Drive | FLB | Kinleith | 59.20000076 | Flashing Lights & Bells |
| Campbell Road | FLB | Kinleith | 60.52000046 | Flashing Lights & Bells |
| Kinleith Road | FLB | Kinleith | 64.59999847 | Flashing Lights & Bells |
| Okoroire Road | HAB | Kinleith | 26.36000061 | Half arm Barriers with flashing lights and bells |
| Main Street | HAB | Kinleith | 35.77000046 | Half arm Barriers with flashing lights and bells |
| Wiltsdown Road | HAB | Kinleith | 46.93000031 | Half arm Barriers with flashing lights and bells |
| Brandon Street | FLB | WL | 56.24000168 | Flashing Lights & Bells |
| Fox Street | FLB | WL | 56.68999863 | Flashing Lights & Bells |
| Bell Street | FLB | WL | 56.91999817 | Flashing Lights & Bells |
| Woodside Road | FLB | WL | 65.33000183 | Flashing Lights & Bells |
| Ferry Road | FLB | MSL | 564.3599854 | Flashing Lights & Bells |
| Dacre-Morton Mains Road | FLB | MSL | 575.4799805 | Flashing Lights & Bells |
| Flemington Road | FLB | MSL | 583.2299805 | Flashing Lights & Bells |
| Longbush South Road | FLB | MSL | 587.8200073 | Flashing Lights & Bells |
| Thornbury Waimatuku Road | FLB | Ohai | 25.67000008 | Flashing Lights & Bells |
| Main Street | FLB | Ohai | 48.65999985 | Flashing Lights & Bells |
| George Street | FLB | Ohai | 50.25 | Flashing Lights & Bells |
| Finnerty Road | FLB | MNPL | 156.3099976 | Flashing Lights & Bells |
| Climie Road | FLB | MNPL | 157.8099976 | Flashing Lights & Bells |
| Hills Road | FLB | MNPL | 160.3600006 | Flashing Lights & Bells |
| Seyton Street | FLB | MNPL | 162.5700073 | Flashing Lights & Bells |
| Pembroke Road | FLB | MNPL | 162.8500061 | Flashing Lights & Bells |
| Beaconsfield Road | FLB | MNPL | 167.4499969 | Flashing Lights & Bells |
| Kent Terrace | FLB | MNPL | 168.0700073 | Flashing Lights & Bells |
| York Road | FLB | MNPL | 169.4799957 | Flashing Lights & Bells |
| Bird Road | HAB | MNPL | 159.3600006 | Half arm Barriers with flashing lights and bells |
| Fenton Street | HAB | MNPL | 161.8800049 | Half arm Barriers with flashing lights and bells |
| Range Road | FLB | PNGL | 28.20000076 | Flashing Lights & Bells |
| Law Road | FLB | PNGL | 51.31000137 | Flashing Lights & Bells |
| Rawhiti Street | FLB | PNGL | 52.29999924 | Flashing Lights & Bells |
| Allardice Street | FLB | PNGL | 53.72000122 | Flashing Lights & Bells |
| Cole Street | FLB | PNGL | 54.65000153 | Flashing Lights & Bells |
| Hospital Street | FLB | PNGL | 55.45999908 | Flashing Lights & Bells |
| Ruahine Street | FLB | PNGL | 55.81000137 | Flashing Lights & Bells |
| Makotuku South Crossing | FLB | PNGL | 70.01999664 | Flashing Lights & Bells |
| Matamau Ormondville Road | FLB | PNGL | 70.65000153 | Flashing Lights & Bells |
| Norsewood Ormondville Rd | FLB | PNGL | 73.45999908 | Flashing Lights & Bells |
| Alfredton Road | FLB | WL | 127.0500031 | Flashing Lights & Bells |
| Haswell Street | FLB | WL | 127.3499985 | Flashing Lights & Bells |
| Hamua-Hukunui Road | FLB | WL | 137.0599976 | Flashing Lights & Bells |
| Hall Street | FLB | WL | 154.4299927 | Flashing Lights & Bells |
| Range Road | FLB | WL | 168.1900024 | Flashing Lights & Bells |
| Stanley Street | HAB | PNGL | 53.09000015 | Half arm Barriers with flashing lights and bells |
| Maxwells Road | FLB | ECMT | 96.48000336 | Flashing Lights & Bells |
| Hamilton Street Ped | FLB | ECMT | 98.15000153 | Flashing Lights & Bells |
| Maungatawa Quarry Road | FLB | ECMT | 106.6100006 | Flashing Lights & Bells |
| Kairua Road | FLB | ECMT | 108.8399963 | Flashing Lights & Bells |
| Totara Street No.3 Sdg | FLB | Mt Maunganui | Flashing Lights & Bells |
| Bureta Road | HAB | ECMT | 95.68000031 | Half arm Barriers with flashing lights and bells |
| Cross Road | HAB | ECMT |  | Half arm Barriers with flashing lights and bells |
| Dive Crescent | HAB | ECMT | 98.01000214 | Half arm Barriers with flashing lights and bells |
| Wharf Street | HAB | ECMT | 98.26999664 | Half arm Barriers with flashing lights and bells |
| Matapihi Road | HAB | ECMT | 101.9599991 | Half arm Barriers with flashing lights and bells |
| Matapihi Road | HAB | Mt Maunganui | 0.970000029 | Half arm Barriers with flashing lights and bells |
| Hull Road | HAB | Mt Maunganui | 4.300000191 | Half arm Barriers with flashing lights and bells |
| Totara Street | HAB | Mt Maunganui | 5.210000038 | Half arm Barriers with flashing lights and bells |
| Rise Road | FLB | MSL | 147.0800018 | Flashing Lights & Bells |
| Springfield Road | FLB | MSL | 150.5 | Flashing Lights & Bells |
| Richard Pearse Drive | FLB | MSL | 152.1999969 | Flashing Lights & Bells |
| Domain Avenue | FLB | MSL | 153.1600037 | Flashing Lights & Bells |
| Arowhenua Station Road | FLB | MSL | 156.3500061 | Flashing Lights & Bells |
| Dominion Road | FLB | MSL | 158.9100037 | Flashing Lights & Bells |
| Heaton Street | FLB | MSL |  | Flashing Lights & Bells |
| Port Loop Rd (North Mole) | FLB | MSL |  | Flashing Lights & Bells |
| Ritchie Street | FLB | MSL |  | Flashing Lights & Bells |
| Orari Station Road | HAB | MSL | 140.8500061 | Half arm Barriers with flashing lights and bells |
| Denmark Street | HAB | MSL | 152.8699951 | Half arm Barriers with flashing lights and bells |
| Seadown Road | HAB | MSL | 163.75 | Half arm Barriers with flashing lights and bells |
| Meadows Road | HAB | MSL | 165.75 | Half arm Barriers with flashing lights and bells |
| Heaton Street | HAB | MSL | 171.3600006 | Half arm Barriers with flashing lights and bells |
| Pareora Avenue | HAB | MSL | 182.3200073 | Half arm Barriers with flashing lights and bells |
| Sutherland Avenue | HAB | WL | 28.87999916 | Half arm Barriers with flashing lights and bells |
| Ward Street | HAB | WL | 31.19000053 | Half arm Barriers with flashing lights and bells |
| Blenheim Street | HAB | WL | 32.02000046 | Half arm Barriers with flashing lights and bells |
| Tauwhare Road | FLB | Cambridge | 7.130000114 | Flashing Lights & Bells |
| Percival Road | FLB | ECMT | 5.949999809 | Flashing Lights & Bells |
| Telephone Road | FLB | ECMT | 11.07999992 | Flashing Lights & Bells |
| Waverley Road | FLB | ECMT | 15.43000031 | Flashing Lights & Bells |
| Island Block Road | FLB | NIMT | 604.2600098 | Flashing Lights & Bells |
| Horotiu Road | HAB | NIMT | 553.9000244 | Half arm Barriers with flashing lights and bells |
| Park Road | HAB | NIMT | 555.539978 | Half arm Barriers with flashing lights and bells |
| Saulbrey Road | HAB | NIMT | 556.5499878 | Half arm Barriers with flashing lights and bells |
| Havelock Road | HAB | NIMT | 557.6099854 | Half arm Barriers with flashing lights and bells |
| Princess Street | HAB | NIMT | 559.4099731 | Half arm Barriers with flashing lights and bells |
| Waingaro Road | HAB | NIMT | 559.6699829 | Half arm Barriers with flashing lights and bells |
| Old Taupiri Road | HAB | NIMT | 560.0599976 | Half arm Barriers with flashing lights and bells |
| Kainui Road | HAB | NIMT | 565.1799927 | Half arm Barriers with flashing lights and bells |
| Tregoweth Lane | HAB | NIMT | 571.8599854 | Half arm Barriers with flashing lights and bells |
| Bell Crossing | HAB | NIMT | 574.5999756 | Half arm Barriers with flashing lights and bells |
| Fletcher Street | HAB | NIMT | 576.2399902 | Half arm Barriers with flashing lights and bells |
| East Mine Road | HAB | NIMT | 577.3900146 | Half arm Barriers with flashing lights and bells |
| Fisher Road | HAB | NIMT | 578.9299927 | Half arm Barriers with flashing lights and bells |
| Te Kauwhata Road | HAB | NIMT | 591.4299927 | Half arm Barriers with flashing lights and bells |
| Oram Road | HAB | NIMT | 606.5999756 | Half arm Barriers with flashing lights and bells |
| Harris Street | HAB | Rotowaro | 0.829999983 | Half arm Barriers with flashing lights and bells |
| Peraki Street | FLB | MNL | 19.38999939 | Flashing Lights & Bells |
| Mulcocks Road | FLB | MNL | 23.34000015 | Flashing Lights & Bells |
| Fernside Road | FLB | MNL | 24.78000069 | Flashing Lights & Bells |
| Boys Road | FLB | MNL | 28.10000038 | Flashing Lights & Bells |
| Northbrook Road | FLB | MNL | 28.88999939 | Flashing Lights & Bells |
| Wales Street | FLB | MNL | 30.45999908 | Flashing Lights & Bells |
| Coldstream Road | FLB | MNL | 31.04000092 | Flashing Lights & Bells |
| High Street | FLB | MNL | 32.97000122 | Flashing Lights & Bells |
| Toppings Road | FLB | MNL | 39.56999969 | Flashing Lights & Bells |
| Harleston Road | FLB | MNL | 41.34999847 | Flashing Lights & Bells |
| Courtenay Drive | HAB | MNL | 18.26000023 | Half arm Barriers with flashing lights and bells |
| Williams Street | HAB | MNL | 19.07999992 | Half arm Barriers with flashing lights and bells |
| High Street | HAB | MNL | 29.71999931 | Half arm Barriers with flashing lights and bells |
| Braddon Street (North) | FLB | MSL | 187.25 | Flashing Lights & Bells |
| Lucks Road | FLB | MSL | 214.7899933 | Flashing Lights & Bells |
| Horsenells Road | FLB | MSL | 218.5200043 | Flashing Lights & Bells |
| Morven Beach Road | FLB | MSL | 220.7400055 | Flashing Lights & Bells |
| Crowes Road | FLB | MSL | 221.7799988 | Flashing Lights & Bells |
| White Street | FLB | MSL | 230.8500061 | Flashing Lights & Bells |
| Foleys Road | HAB | MSL | 210.2899933 | Half arm Barriers with flashing lights and bells |
| Te Mawhai Road | FLB | NIMT | 513.0900269 | Flashing Lights & Bells |
| Forkert Road | FLB | NIMT | 527.6500244 | Flashing Lights & Bells |
| Rukuhia Road | FLB | NIMT | 533.4899902 | Flashing Lights & Bells |
| Alexandra Street | HAB | NIMT | 517.4500122 | Half arm Barriers with flashing lights and bells |
| Collins Road | HAB | NIMT | 538.3800049 | Half arm Barriers with flashing lights and bells |
| Ormond Drive | FLB | PNGL | 335.8500061 | Flashing Lights & Bells |
| New Lynn Ped | FLB | NAL | 19.48999977 | Flashing Lights & Bells |
| Corbans Ped | FLB | NAL | 27.13999939 | Flashing Lights & Bells |
| Oneills Road Ped | FLB | NAL | 31.38999939 | Flashing Lights & Bells |
| Portage Road | HAB | NAL | 18.87999916 | Half arm Barriers with flashing lights and bells |
| Veronica Street | HAB | NAL | 19.07999992 | Half arm Barriers with flashing lights and bells |
| Totara Avenue | HAB | NAL | 19.55999947 | Half arm Barriers with flashing lights and bells |
| Fruitvale Road | HAB | NAL | 20.94000053 | Half arm Barriers with flashing lights and bells |
| Glenview Road | HAB | NAL | 22.43000031 | Half arm Barriers with flashing lights and bells |
| Sherrybrooke Place | HAB | NAL | 24.20000076 | Half arm Barriers with flashing lights and bells |
| Bruce McLaren Road | HAB | NAL | 25.54999924 | Half arm Barriers with flashing lights and bells |
| Mt Lebanon Lane | HAB | NAL | 27.37000084 | Half arm Barriers with flashing lights and bells |
| Metcalfe Road | HAB | NAL | 29.5 | Half arm Barriers with flashing lights and bells |
| Christian Road | HAB | NAL | 32.36000061 | Half arm Barriers with flashing lights and bells |
| Robertson Road | FLB | MSL | 238.1300049 | Flashing Lights & Bells |
| Richmond Road | FLB | MSL | 243.4600067 | Flashing Lights & Bells |
| Redcastle Road | FLB | MSL | 250.5200043 | Flashing Lights & Bells |
| Waitaki Avenue | FLB | MSL | 251.2200012 | Flashing Lights & Bells |
| Caledonian Road | FLB | MSL | 252.0099945 | Flashing Lights & Bells |
| Weaver Street | FLB | MSL | 252.7299957 | Flashing Lights & Bells |
| Orwell Street | FLB | MSL | 252.8000031 | Flashing Lights & Bells |
| Thames Street | FLB | MSL | 254.6199951 | Flashing Lights & Bells |
| Solway Street | FLB | MSL | 256.3999939 | Flashing Lights & Bells |
| Thousand Acre Road | FLB | MSL | 259.6300049 | Flashing Lights & Bells |
| Glencoe Road | FLB | MSL | 277.3500061 | Flashing Lights & Bells |
| Moeraki Boulders Road | FLB | MSL | 292.6499939 | Flashing Lights & Bells |
| Moeraki Road | FLB | MSL | 293.8299866 | Flashing Lights & Bells |
| Goodwood Road | FLB | MSL | 315.3900146 | Flashing Lights & Bells |
| Works Road | HAB | MSL | 245.7299957 | Half arm Barriers with flashing lights and bells |
| Regina Lane | HAB | MSL | 251.5299988 | Half arm Barriers with flashing lights and bells |
| Coquet Street | HAB | MSL | 254.0500031 | Half arm Barriers with flashing lights and bells |
| Ross Road | HAB | MSL | 276.0799866 | Half arm Barriers with flashing lights and bells |
| Waimiha Road | FLB | NIMT | 447.1400146 | Flashing Lights & Bells |
| Te Kumi Station Road | FLB | NIMT | 479.2099915 | Flashing Lights & Bells |
| Ward Street | HAB | NIMT | 476.2000122 | Half arm Barriers with flashing lights and bells |
| Rora Street | HAB | NIMT | 476.519989 | Half arm Barriers with flashing lights and bells |
| Mangarino Road | HAB | NIMT | 485.4400024 | Half arm Barriers with flashing lights and bells |
| Okoia Road | FLB | MNPL | 35.61000061 | Flashing Lights & Bells |
| Western Line | FLB | MNPL | 49.97999954 | Flashing Lights & Bells |
| Kaikokopu Road | FLB | Wanganui | 0.200000003 | Flashing Lights & Bells |
| Barrack Street | FLB | Wanganui | 0.870000005 | Flashing Lights & Bells |
| Halswell Street | FLB | Wanganui | 1.350000024 | Flashing Lights & Bells |
| Pitt Street | FLB | Wanganui | 1.600000024 | Flashing Lights & Bells |
| Harrison Street | FLB | Wanganui | 1.960000038 | Flashing Lights & Bells |
| Glasgow Street | FLB | Wanganui | 2.75999999 | Flashing Lights & Bells |
| Liverpool Street | FLB | Wanganui | 2.99000001 | Flashing Lights & Bells |
| Purnell Street | FLB | Wanganui | 3.819999933 | Flashing Lights & Bells |
| Taupo Quay | FLB | Wanganui | 4.679999828 | Flashing Lights & Bells |
| Heads Road | FLO | Castlecliff | 3.670000076 | Out of use |
| Holyoake Street | HAB | MNPL | 41.81000137 | Half arm Barriers with flashing lights and bells |
| Poutini Street | HAB | MNPL | 42.38000107 | Half arm Barriers with flashing lights and bells |
| Somme Parade | HAB | MNPL | 42.86999893 | Half arm Barriers with flashing lights and bells |
| Victoria Avenue | HAB | Wanganui | 2.450000048 | Half arm Barriers with flashing lights and bells |
| College Street | HAB | Wanganui | 3.599999905 | Half arm Barriers with flashing lights and bells |
| Guyton Street | HAB | Wanganui | 4.150000095 | Half arm Barriers with flashing lights and bells |
| Simla Crescent | HAB | Johnsonville | 6.829999924 | Half arm Barriers with flashing lights and bells |
| Station Road | HAB | Johnsonville | 7.940000057 | Half arm Barriers with flashing lights and bells |
| Fraser Avenue | HAB | Johnsonville | 8.81000042 | Half arm Barriers with flashing lights and bells |
| Waterloo Quay (South) | HAB | NIMT |  | Half arm Barriers with flashing lights and bells |
| Waterloo Quay (North) | HAB | NIMT |  | Half arm Barriers with flashing lights and bells |
| Tawa Street | HAB | NIMT | 13.05000019 | Half arm Barriers with flashing lights and bells |
| McLellan Street | HAB | NIMT | 14.52000046 | Half arm Barriers with flashing lights and bells |
| Collins Avenue | HAB | NIMT | 15.09000015 | Half arm Barriers with flashing lights and bells |
| Paparoa Road | FLB | ECMT | 87.05000305 | Flashing Lights & Bells |
| Bell Road | FLB | ECMT | 113.0500031 | Flashing Lights & Bells |
| Kenana Road | FLB | ECMT | 122.2699966 | Flashing Lights & Bells |
| Pah Road | FLB | ECMT | 123.6900024 | Flashing Lights & Bells |
| Pongakawa School Road | FLB | ECMT | 134.2700043 | Flashing Lights & Bells |
| Pongakawa Station Road | FLB | ECMT | 135.2200012 | Flashing Lights & Bells |
| Maketu Road | HAB | ECMT | 125.8300018 | Half arm Barriers with flashing lights and bells |
| Park Street | FLB | Hokitika | 37.93000031 | Flashing Lights & Bells |
| Hampden Street | FLB | Hokitika | 38.16999817 | Flashing Lights & Bells |
| Otira Settlement Road | HAB | Midland | 130.1300049 | Half arm Barriers with flashing lights and bells |
| Manawahe Road | FLB | ECMT | 161.5200043 | Flashing Lights & Bells |
| Simpsons Crossing | FLB | ECMT | 163.7599945 | Flashing Lights & Bells |
| Western Drain Road | FLO | Taneatua | 9.170000076 | Out of use |
| Tauraroa Road | FLB | NAL | 187.4100037 | Flashing Lights & Bells |
| Kioreroa Road | FLB | NAL | 211.75 | Flashing Lights & Bells |
| Manse Street | FLB | NAL | 215.0899963 | Flashing Lights & Bells |
| Wrack Street | FLB | NAL | 215.5399933 | Flashing Lights & Bells |
| Kensington Avenue | FLB | NAL | 215.7799988 | Flashing Lights & Bells |
| Kamo Road | FLB | NAL | 216.3699951 | Flashing Lights & Bells |
| Saleyards Road | FLB | NAL | 226.0299988 | Flashing Lights & Bells |
| Valley Road | FLB | NAL | 232.1000061 | Flashing Lights & Bells |