## Slide 1
Understanding Road Users
Traffic & Road Safety Research Group Waikato University
  Samuel G. Charlton

## Slide 2
Applied Cognitive Psychology
Applying what we know about people, how they think and behave, their characteristics, requirements and and designing tools, procedures, and systems to fit them
Mātai hinengaro whaipainga me te roro tāiao
Human Factors
Ergonomics
Engineering Psychology
Human-centered design
Soft technology designing the tool to fit the user
Hard technology the user has to fit the tool

## Slide 3
People make mistakes
1
People are vulnerable
2
We need to share responsibility
3
We need to strengthen all parts of the system
4
Human-centered design is at the heart of the Safe System philosophy

## Slide 4
Old Approach | Safe System approach
Tell people to ‘get with the system’ | Design systems around people
Blame road users when things go wrong | Understand people and the tasks they do
Address the immediate issues only | Consider all factors that lead to crashes
Human factors – people first

## Slide 5
Road transport should be as easy and safe to use as a consumer product
Why study driver behaviour?
A very good applied area for studying cognition
human performance, attention & decision making
A common skill we acquire as young adults
Significant public health issue
1.3 million people killed on the roads each year worldwide forecast to rise to 1.9 million people by 2020 World-wide 3,400 people die on the road every day Number one cause of death for young people 50 million people injured, many remaining disabled for life

## Slide 6
Knowledge
Environment
Skills
Modifies
Directs
Samples
Perceptions
Decisions
Actions
10,000 PDA cycles per hour on a straight road
Individual thoughts and actions repeated together often enough become combined into a single unit
an open-loop (ballistic) program or script
Highly practised tasks become automatic
The Perception-Decision-Action (PDA) Cycle
Driving as a skill

## Slide 7
1) Perception stage – Effective field of vision
The driver’s eye cannot take in the whole roadway with acuity Foveal vision is 2° - 4°
Drivers use rapid fixations to take in the scene
100 – 300 msec for lane position
2 sec for estimating speed and distance or reading road signs
50 km/h = 14m per sec 100 km/h = 28m per sec
Horizontal field of vision = 150° at 50 km/h Horizontal field of vision = 50° at 100 km/h Effective field of vision becomes narrower and deeper

## Slide 8
1) Perception stage -- channelised attention

## Slide 9
2) Decision stage – comprehending & planning
We use working memory to identify situations, make conscious decisions, apply rules, solve problems, etc.
Working memory is limited in capacity and conscious thought takes time
Notes: compressed

## Slide 10
The effect of reduced field of vision & time compression in decision making: We steer where we look (DWA)
3) Action stage

## Slide 11
Looked-but-failed-to-see crashes
(Brown, 2005; Treat, 1980; White & Caird, 2010)
collisions in which a driver fails to detect another road user or object despite looking at it
Third most frequently occurring driver error
(SMIDSY)
Highly practised tasks become automatic
Most drivers are driving without awareness, most of the time
Why do looked-but-failed-to-see crashes occur?
Looked-but-failed-to-see crashes
appear to predominate on familiar roads
(Brown, 2002; Hills, 1980; Kousanaï, Boloix, van Elslande, & Bastien, 2008; Rumar, 1990; Treat, 1980; White & Caird, 2010)

## Slide 12
All participants developed stereotyped driving patterns Speed and lane position became less responsive
Driving Without Awareness
29 participants drove a simulated road twice a week for approx 12 weeks
13 males, 16 females
Mean age = 30.17 years (ranged 17 to 49 years)
Participants noticed fewer and fewer things in their environment
(Charlton & Starkey, 2011, 2012, 2013)

## Slide 13
Driving Without Awareness
Change detection sessions: changes to or removal of road markings, road signs, buildings, etc
Participants noticed fewer and fewer things in their environment
Participants did not detect removal of prominent buildings or changes from English to German wording
Participants developed stereotyped driving patterns

## Slide 14
Road works trials
Drivers reduced their speeds well before entering the site
First time through the road works
Second and subsequent times
Drivers noticed the sites earlier and earlier but slowed down less and less

## Slide 15
Two modes of driving
Supervisory level
Procedural level
learning to drive, navigating in an unfamiliar area, overtaking, controlling a skid on ice
speed maintenance, lane position, following distances, brake reactions, changing lanes, eye scanning, checking mirrors, negotiating a familiar intersection, school zones,
approaching and driving through curves, entering traffic
explicit attention
automatic procedures
10%
90%

## Slide 16
Charlton & Starkey’s Tandem Model an “operating process” and “monitoring process” working in tandem
Operating process: conscious, intentional decision making, uses deliberate search of environment, requires effort and can be undermined by distractions
Monitoring process: an unconscious error monitoring system, requires little cognitive effort, continuously active, rapid error detection, sufficient to maintain many aspects of driving (esp. on familiar roads)
Proceduralisation (automaticity) represents a broadening and refinement of the templates (schemata) used by the monitoring process
Driving without awareness (DWA)
Much of our driving behaviour is governed implicitly esp. lane keeping & speed maintenance

## Slide 17
#1 change detected by drivers – removal of centrelines #2 – removal of edgelines
Driving without awareness (DWA)
We steer where we look
Monitoring process: relies on the presence of familiar cues When potential failure stimulus is detected, the object receives additional activation until the operating process returns conscious attention to task

## Slide 18
SH1 Before
SH1 After
South Waikato & Taupo Target 2010 Project
Pre treatment
Phase 1
Phase 2
Significant safety gain with no increase in speed
Rural delineation treatments

## Slide 19
Drivers didn’t notice the changes
Addition of continuity lines resulted in more drivers keeping left
Lane Delineation Treatments
(Charlton et al 2001 ; Charlton 2007)

## Slide 20
The effect of removing lane delineation: One of the most effective merge treatments for overtaking lanes
(Drivers hated it: increased perceived risk)
Dashed side line: max 80 kph.
Continuous middle line: no overtaking
Continuous side line: max 100 kph.
Continuous middle line: no overtaking
Green line in middle: absolutely 100 kph
Dashed side line only: max 60 kph.
Bicycles only in red lane
Bicycles on road
overtaking allowed
We could make better use of road markings

## Slide 21
Most common way of communicating information to drivers is via road signs
Drivers may notice as few as 1 in 10 road signs and have very poor memory for road signs they’ve just passed (6% recall - 9% recognition)
Assessment of Hazard Warning Signs
25.81%
38.46%
12.90%
19.35%
41.94%
(Charlton, 2006)
What cues do drivers use?

## Slide 22
Fitzgerald Glade SH5
The look and feel of a road determines how it is used
Much of our driving behaviour is governed implicitly esp. lane keeping & speed maintenance

## Slide 23
Optic flow drivers use edge rate in the visual environment to judge their speed (preconsciously)
increasing the visual edge rate increases drivers’ sense of speed

## Slide 24
We can use psychological principles to affect the “look & feel” of a road
Choosing road widths, delineation, and road furniture designed to afford a desired speed and lane position
Affordances: perceptual properties that function as “built-in” instructions, processed without awareness

## Slide 25
Access roads
Distributor roads
Through roads
Sustainable Safety – The Netherlands
Differentiating the road hierarchy

## Slide 26
These NZ roads look very similar
Currently, we don’t do a very good job at telling drivers what kind of road they are using
50
60
70
80
100
but they all have different speed limits

## Slide 27
These three NZ roads all have the same speed limit, 100 km/h
Self-Explaining Roads for Sustainable Safety Programme (Liveable Streets)
Funded by Foundation for Research Science & Technology
Using psychological principles to affect the “look & feel” of a road

## Slide 28
Control Area
Treatment Area
Need to monitor two areas to quantify the effectiveness of the SER designs
Glen Innes / Pt England
Step 1: Select trial area

## Slide 29
Pt England Rd Collector road 5,000-7,000 vpd
Anderson Ave Local road 377 vpd
(high intersection crash rate)
Existing streetscapes didn’t provide enough information about the road hierarchy or appropriate use of the streets
SER requires a clear hierarchy of roads
Self-Explaining Roads for Sustainable Safety Programme (Liveable Streets)

## Slide 30
What is good about these streets? Which ones are working?
Develop a template around those features that visually reinforce the appropriate speeds
Make each level in the hierarchy Visually Distinct and promote the correct uses at each level
Steps 4-5: Analyse existing road features & develop SER design template

## Slide 31
Participatory design for self-explaining roads

## Slide 32
Participatory design for self-explaining roads

## Slide 33
Local roads
Collector roads
Development of an SER design template
for Glen Innes / Pt England

## Slide 34
Steps 6-9: Implementation planning, community input & design reviews

## Slide 35
Implementation
Cost could not exceed amount already budgeted for “minor safety improvements”

## Slide 36
Before
Local roads
Collector roads

## Slide 37
After
Local roads
Collector roads

## Slide 38
Percent of vehicles
Pre-treatment speeds
0
10
20
30
40
50
60
70
80
90
100
Speed (km/h)
Local road
Collector road
0
5
10
15
20
25
30
35
40
45
50

## Slide 39
Percent of vehicles
Post-treatment speeds
0
10
20
30
40
50
60
70
80
90
100
Speed (km/h)
Local road
Collector road
0
5
10
15
20
25
30
35
40
45
50
Different speed profiles for different road categories

## Slide 40
Results
A decrease in local road speeds Significant homogeneity of speeds
No speed signs
No enforcement
Self-Explaining Roads
30% reduction in crashes
86% reduction in crash costs
Health benefits 3x the road safety benefits
Safer Journeys 2010
The government will work to improve our roads so that each type of road will eventually have a recognisable and distinctive set of self-explaining features such as signage, lane width, road markings and speed limits. This work will ensure roads are predictable … should encourage people to travel at speeds that best fit the design and function of the road.
Charlton et al (2010) Using endemic road features to create self-explaining roads and reduce vehicle speeds. Accident Analysis and Prevention

## Slide 41
Is driving with a 0.05 BAC any safer than driving at 0.08?
Drunker Than You Think: Delayed Performance Impairment From Moderate Amounts Of Alcohol
1. Evaluate the biphasic effects of .05 and .08 alcohol levels on psychomotor, cognitive, and driving performance
2. Identify the relationship between drivers’ self-perception of intoxication and the actual level of performance impairment produced
2 research questions:

## Slide 42
Acute tolerance (Mellanby Effect) lower impairment on the descending limb of the intoxication curve as compared to the same BAC on the ascending limb
Acute protracted error greater impairment on the descending limb of the intoxication curve as compared to the same BAC on the ascending limb
BAC
Impairment
acute protracted error
descending limb
ascending limb
BAC
Impairment
acute tolerance
descending limb
ascending limb
Biphasic effects

## Slide 43
Method
Randomly assigned to 3 alcohol dose groups: placebo, medium (.05), or high (.08)
61 participants 33 males 28 females average age of 31.11 years (SD = 8.34)
5 Test blocks (approx 3.5 hrs)
Each test block triggered by elapsed time
30% vodka, 70% orange juice divided equally across three drinks
Two drinks given after baseline testing, 5 minutes to consume each drink
Third drink given 35 mins later unless BAC within .01 of target

## Slide 44
Performance Measures
CogState test battery
Driver Attention Inhibition & Reaction (DAIR) test
Walk & turn test NZ Police Compulsory Impairment Test
Timed Chase Test
Groton Maze Learning Task (GMLT)
Card identification Task (RT)
GMLT Recall Task
Speed, lane position, hazard reactions
Self-ratings of intoxication & willingness to drive

## Slide 45
Results
Participants were unable to judge how much alcohol they had consumed
.08 BAC participants’ estimates not significantly different than .05 participants (about ½ as much as they actually consumed)

## Slide 46
Willingness to drive
Subjective intoxication
GMLT recall errors
3 measures showed acute tolerance
6 measures showed acute protracted error
Chase task errors
Chase task speed
Sec over the centre line
Centre line crossings
Sec over 100 km/h
GMLT errors
6 measures showed symmetric dose-dependent effects (no difference between ascending and descending limbs)
Results

## Slide 47
Symmetric dose-dependent effects
More alcohol = more impairment
No difference due to time
Sec over the edge line
Significant BAC effects
F(2,45) = 5.332, p = .008, ηp2 = .192
False alarm responses
F(2,45) = 4.168, p = .022, ηp2 = .156

## Slide 48
Acute Tolerance Effects
Willingness to drive rating
Subjective intoxication rating
Impairment decreases faster than BAC (you feel less drunk than you are)
*
* Pairwise comparisons p < .05
*
Significant BAC & phase effects

## Slide 49
Acute Protracted Error
Impairment increases with time (even though BAC hasn’t changed)
* Pairwise comparisons p < .05
Significant BAC, phase, & interaction effects
Sec over 100 km/h
*
*
Chase task errors
*

## Slide 50
Would acute tolerance and acute protracted error still be evident if participants were intoxicated for longer periods?
Are these effects found in “normal” drinking?
Usually people consume alcohol in groups,
with smaller drinks over longer periods of time
Study 2 -- Research goals
2. Determine whether Acute Tolerance and Acute Protracted Error occur with longer peak alcohol plateau (habituation effects)
1. Assess the effect of other drinkers’ presence (expectancy effects)

## Slide 51
Tested in groups of three (random selection)
44 participants 21 males 23 females average age of 32.84 years (SD = 8.49)
Alcohol administered ad libitum until desired BAC levels obtained, maintained at peak for 1 hour
5 Test blocks
BAC
Block 5 descending limb (.03 or .05)
Block 1 baseline
1
2
3
4
5
Block 3 peak 1 (.05 or .08)
Block 4 peak 2 (.05 or .08)
Block 2 ascending limb (.03 or .05)
Method
Three alcohol dose groups: placebo, medium (.05), or high (.08)

## Slide 52
Measures
Driver Attention Inhibition & Reaction (DAIR) test
CogState test battery
Self-ratings of intoxication & willingness to drive

## Slide 53
Subjective intoxication
Placebos reported being as intoxicated as the Med and High alcohol groups

## Slide 54
No acute tolerance effect
Solo Placebo significantly lower than Placebo & .08 groups (p < .028)
Compared 20 Solo Placebos from previous study to the 3 social drinking groups in the current study
Subjective intoxication

## Slide 55
Drink estimation
Solo Placebo significantly lower than all other groups (p < .036)
Participants were unable to judge how much alcohol they had consumed

## Slide 56
Cognitive & driving performance
4 measures showed acute protracted error
4 measures showed symmetric alcohol effects (no difference between ascending and descending limbs)
SDLP
Sec over the centre line
Centre line crossings
GMLT rule break errors
GMLT recall errors
Chase task errors
0 measures showed acute tolerance
Maximum speed
Sec over 100 km/h

## Slide 57
Sec over the centre line
Centre line crossings
Symmetric Alcohol Effects
More alcohol = more impairment (note impairment displayed by Social Placebos)
No difference due to time
Significant BAC effects

## Slide 58
Acute Protracted Error
Sec over 100 km/h
Maximum speed
*
*
Impairment increases with time (even though BAC hasn’t changed)

## Slide 59
Conclusions
1. Participants were unable to judge how much alcohol they had consumed or their level of intoxication (expectancy effects)
2. Alcohol dose effects and acute protracted error were found even with lengthy BAC plateau and moderate amounts of alcohol (no habituation effects)
3. Acute tolerance of intoxication judgements were not found with longer social drinking
Charlton & Starkey (2015) Driving while drinking: Performance impairments resulting from social drinking. Accident Analysis & Prevention.
Starkey & Charlton (2014) The effects of moderate alcohol concentrations on driving and cognitive performance during ascending and descending BACs. Human Psychopharmacology: Clinical and Experimental.

## Slide 60
Is talking on a cellphone while driving any riskier than conversing with a passenger?
Compared 4 groups of drivers
Drivers conversing with a passenger
Drivers conversing on a hands-free cellphone
Drivers conversing with a remote passenger
No conversation (control)
Driving while conversing: Cellphones that distract and passengers who react

## Slide 61
Hazard 1 - Busy intersection
Hazard 2 - Parked car entering traffic
Hazard 3 - One-lane bridge
Participants drove a simulated 25 km road containing 5 hazards & an overtaking lane
Hazard 4 - Road works
Hazard 5 - Land slip
Overtaking lane

## Slide 62
Controls and drivers talking to a passenger slowed down as they approached a hazard, braked earlier and further away from hazards
Drivers talking on cellphones had significantly more crashes
Conversation suppression: when the passenger saw an approaching hazard, they stopped talking
Conversation complexity: cellphone conversors made longer (and more difficult) utterances
SA enhancement: passengers discussed the road & often alerted the driver to hazards

## Slide 64
Talking on a cellphone while driving is different than conversing with a passenger
Talking on a hands-free cellphone while driving is just as dangerous as talking on a handheld phone
Conclusions
Wilson, Thomson, Starkey, & Charlton, (2013). Persisting mobile phone use while driving and possible solutions for New Zealand. The New Zealand Medical Journal.
Charlton (2009) Driving while conversing: Cell phones that distract and passengers who react. Accident Analysis and Prevention.

## Slide 65
Option 1: Raise the driving age
Option 2: Lower the driving age
In NZ, 15-19 yr old drivers are 7% of the driving population, but are involved in 14% of fatal crashes (10% male, 4% female)
In NZ, older drivers are over-represented in their rates of intersection crashes and fatigue-related crashes
Its always tempting to concentrate on “High Risk” drivers

## Slide 66
Option 3: Get tough on recidivist drunk drivers
16% of drivers treated at Midland Region Trauma Service
are over the legal BAC limit
Option 4: Get tough on drunk walkers
56% of pedestrians treated at Midland Region Trauma Service
are over the legal BAC limit
Concentrate on “High Risk” drivers

## Slide 67
Option 5: Don’t allow driving in Northland & Waikato
Northland: 3.6% of the population but 6.8% of the social cost of crashes
Waikato: 9.4% of the population but 15.4% of the social cost of crashes.
Concentrate on “High Risk” drivers

## Slide 68
Option 6: Don’t allow women from Whangarei to drive
The highest rates collision across the two islands come from Whangarei women, who reported an incidence of at-fault collisions of 2.5 times the national average
Kirsty Nelson
first woman ever to win the Hella International Rally
Concentrate on “High Risk” drivers

## Slide 69
We like to blame other drivers for the road toll

## Slide 70
George Carlin 1984
Have you ever noticed that anybody driving slower than you is an idiot, and anyone going faster than you is a maniac?
We like to blame other drivers for the road toll

## Slide 71
We like to blame other drivers for the road toll

## Slide 72
It’s not the other drivers *it is us*

## Slide 73
A Safe System approach
Vehicles (Machine factors)
Roads (Task factors)
Drivers (Human factors)
Providing roads that are self-explaining & self-enforcing
Providing vehicle safety equipment & decision support information
Providing training & education for an engaged and safety-conscious road user population
Use research to inform policy & practice
Traffic & Road Safety Research Group Waikato University