## Slide 1: Raising the Bar
Ivan Aplin
Representing the minor Sports!

## Slide 2: Background
Cycling New Zealand
  President – 3 years up to May 2015
  Commissaire
Practicing STMS Involved only in Approx. 40 events pa.
Trainer up to recently only specialised in Events.

## Slide 5: To raise the bar you must understand and acknowledge events require different TTM in some cases

## Slide 6: Event Sites are not Work Sites

## Slide 7: TTM is different for Running, Triathlon and Cycling Events
Notes: When setting out the worksite vehicles must have flashing beacons on (hazard lights do not count)
Work out where your signs are going (start with the working space required and work out from there)
Place the advance warning sign
Place the next sign if required
Drop your cones off
Place the next sign if required
Place the end of works sign
Go down the road, turn around
Place the advance warning sign
Place the next sign if required
Place the next sign if required
Place the end of works sign
Go down the road, turn around
Under the protection of a vehicle setup your taper
If it is a short site set out the cones down the side of the worksite as well
If longer worksite drive off. The cones along the side of the worksite can be set out safely as the taper has moved the traffic past the worksite
Tapers and delineation devices must only be placed once all signs have been installed
Once the site is setup immediately complete a drive through, checking that the site works as required
Once you have checked the site it can be occupied with workers and equipment

## Slide 8: Fun Events need different considerations

## Slide 9: As do the number of participants

## Slide 10: Cones are a Hazard for cyclists

## Slide 11: Events such as concerts/markets need other different consideration

## Slide 12: Such as Increased traffic & Parking

## Slide 13: With declining Police support – we need to review options for rolling road blocks
Can we get some sort of permitting system for STMS?

## Slide 14: Main issues experienced by our clubs
The cost of TTM Equipment & Training
Volunteers’ time
Vehicles used to set up
Consistency across RCA
Decrease in Club Membership/racing
Increase in “underground cycling groups” who fall outside Cycling New Zealand and there rules

## Slide 15: Other Issues
Resource consent required
Sending in On Site forms for events only
Touring groups
  If No Pilot and Tail vehicles - falls out side CoPTTM (road rules apply!)
  Add in Pilot and Tail need a TTM Plan
Greater clarity around Mobile Operations for Cycle races

## Slide 16: A.4 Levels of Road
  Level 1 (Up to 10,000vpd)
  Low Volume (Up to 500vpd)
  Low volume/low risk (Less than 250vpd)
Roads
Events
  Level 1 (Big Events)
  Low Volume (Small)
  Low volume/low risk (Small/Low Risk)
A.4b Levels of Events

## Slide 17: Examples
Rural School – Motocross LV Roads. Advance warning signs only.
Urban High School - Annual run around the block – mainly foot paths but one leg on the road. All 50 staff on the course! STMS must be on site.
Hockey event. Advance warning only. Required to do 2 hourly inspections

## Slide 18: Gating Speed Signs
Why do Events have to? - when others do not!
  3 very recent examples
  Urban Road- over 3850 vpd and not gated!
  Rural Rd with Est 3,000 vpd and not gated!
  1.4km Rd over 10,000 vpd not gated nor repeaters!

## Slide 19: We need to
Start adding to section I.3 (Reversed for events) of the CoPTTM.
Create some forum discussions on events.
Improve knowledge/sharing best practices of events TTM.
Relook at training material.
Briefings Include as part of TMP?
CoPTTM
RCA
Sports

## Slide 20: Questions/Discussion?

## Slide 21
Exercise

## Slide 22
Single land Road
70 km therefore lanes Width 3.25m
Busy Rd
4.4m
At Crossing Lane 1 - 4.4m
Lane 2 - 4.5m
At Intersection Lane 1 - 4.4m
Lane 2 - 4.6m
Centre Line 38m long
Min Width 5.5m max width 6.0m

## Slide 23
Option 1
Create lane for Cyclist

## Slide 24
Option 2
Create lane for Cyclist and Lane shift

## Slide 25
Option 3
Lane closed sign added

## Slide 26
Option 4
Lane Narrows

## Slide 27
Option 5
Take out whole lane

## Slide 28: Who suggest what
Option 1 - Just create lane
Option 2 - Create lane and move 1 lane over
Option 3 - Lane closure
Option 4 - Road Narrows
Option 5 - close whole lane
Option 6 – Don’t let the event go ahead full stop. Bored don’t care.